FE4P25-35Q-SMS-001

WARNING

Do not use the forklift before reading and understanding the operating instructions as well as the waring decals on the truck.

Keep for future reference.

Operation  manual

FE4P25-35  Q series

battery counterbalanced forklift truck

NOBLELIFT INTELLIGENT EQUIPMENT CO.,LTD.

Catalogue

Introduction	3

Chapter one Attentions when using the forklift truck	4

1 .Transportation for forklift	4

2. Deposit	4

3. Preparation before use	4

4. Operation of truck	4

5. Lithium Battery charging	5

Chapter two The main performance parameters of forklift truck	6

Ⅰ.The truck’s outline dimension and performance parameters.	6

1. The truck’s outline dimension  see figure 1-1	6

2.Technical data	7

Chapter Three Operation,use and safety for forklift	8

Ⅰ.Driving and operation	8

1. Usage of new vehicle	8

2. Connection between load and stability	8

3. Load center and load curve	8

4. Forklift stability	8

5. Transporting and loading for forklift	9

6. Preparation before driving	9

7. Steer	9

8. Parking and temporary parking	10

9. Usage of battery	11

10．Stacking	12

11．Unstacking	13

12 Deposit	13

Ⅱ.Using instruction of operating devices	14

1. Components,schematic diagram for operating devices（see following figure）	14

2. Instrument unit	15

3. Switches	15

4. Control	16

5. Truck body	18

Ⅲ.Safety issues	20

1. Operation place and working environment	20

2. Safety rules	20

3. Move the truck	30

4. How to avoid overturning,how to protect yourself	31

5. Safety problem in Maintenance	32

6. Safety problem in battery usage	34

Chapter four Electrical system	36

1 Electric control assembly（Curtis）	36

2 Main functions and settings	38

3 Maintenance of circuit system	38

4 Combination instrument	39

5 Failure analysis	40

Chapter five Truck’s regular check and maintenance	45

Ⅰ.The check before operation	45

1. Checking point and checking content	45

2. Checking procedure	46

Ⅱ.Check after operation	50

Ⅲ.Truck cleaning	50

1. Truck surface cleaning .	50

2. Chains cleaning	50

3. Electric system cleaning	51

4. After cleaning	51

Ⅳ.Regular maintenance	51

1. Regular maintenance schedule	51

2. Regular replacement of key safety parts	56

Ⅴ.Area lubricated and lubricant recommended	57

1. Area lubricated	57

2. Lubricant recommended	58

3. Hydraulic Schematic Diagram	58

4. labeling	59

Chapter six Truck’s Lithium battery use and safety	60

1. Safety operation procedures	60

2. Introduction and application requirements of lithium batteries	61

3. Charging operation instructions for lithium batteries	63

4. Structure and main technical parameters of lithium battery	65

5 Transportation	69

## Introduction

This manual briefly describes the technical parameters of the counterbalanced accumulator forklift made by our company, and the structure of its main components, working principle and requirements on operation and maintenance. Please read this manual carefully before operation, so as to achieve proper driving and maintenance, and to ensure safe and effective material handling. Meanwhile, this manual aims to guide operators to use the forklift in an appropriate way and to maximize its performance! We hope that operators and equipment managers could read it carefully before use! Please strictly observe the provisions and cautions stipulated in this manual and operate the forklift with caution and care, so that the forklift can be maintained in its best status and optimal performance can be ensured. When you lease or transfer your forklift, always keep this manual with it.

For highlighting purpose, the following icons are used in this manual:

1.    ----Refers to a potential danger; if not avoided, it may cause serious human injury, vehicle damage or fire.

2. ----Refers to a potential danger; if not avoided，it may cause minor human injury, or local damage to the vehicle.。

3. ----Refers to general cuations and instructions during use.

Most parts of the product are made from recyclable steel. The recycling and disposal of cast-offs resulted during use, maintenance, cleaning and disassembling of the product has to comply with local regulations without pollution to the environment. The recycling and disposal of the cast-offs should only be operated by specialised personnel in the designated area. The cast-offs, such as hydraulic oil, batteries and electronic units, if improperly disposed, may be hazardous to the environment and human health.

4）The normal use of the product's environmental requirements as follows: no more than 2000 meters above sea level and the temperature range of+5 ° C - +40 ° c, humidity should no more than 90%.The wind speed is not more than 5m/s.

If you need to use in the freezer for a long time, Or in special environment, it is needed to install special attachments. Please contact our technical staff.

5）Product recall serive is available when serial faulties occur.

Due to continuous product improvement, Noblelift reserves the right to make changes in product designs and specifications without prior notice. For the latest product parameters, please feel free to contact us. All parameters provided herein are as of the publication date of the Instruction Manual.

# Chapter one Attentions when using the forklift truck

The operator mast always keep in mind the principle of safety first.Conscientiously and cautiously read the maintenance manual.Undergo safe operate and canonical operate strictly following the demand in this manual

## 1 .Transportation for forklift

Pay attention to the following particulars when using container or automobile to convey forklift truck

(1) Enable parking brake

(2) Fasten mast and counterweight with steel wire in both two sides;Chock with wedge the

front and rear wheels at propor site

(3) Hoist Lift the forklift according to indication on lifting plate

## 2. Deposit

(1) Lower the mast to the lowest position

(2) Switch off power,Push all the operating rod to vacancy;Pull out power plug

(3) Stretch hand brake rod

(4) Chock with wedge front and rear wheels

(5)When truck is in long-term non-use.Wheels should be overhead.And battery should be boost charged once a month

## 3. Preparation before use

(1) Check up all the meters

(2) Check up tire pressure

(3) Check up the state of each handle and pedal

(4) Check up if the voltage of battery is in operating range;and weather the specific density of electrolyte and the altitude of liquid surface are in order

(5) Check up if the contact of each connector and plug of electrical system is ok

(6) Check up if the hydraulic liquid,electrolyte or brake fluid is leaking

(7) Check up the condition of each main fastener

(8) Check up if the illuminators,signal lamps are in order

(9) Loosen parking brake

(10) Try to lift and lower the mast,tilt forward and backward the mast,turn and brake the truck

(11) Be sure that the polluting level of hydraulic oil is less than 12grade

## 4. Operation of truck

(1) Only can the person operate the truck who has been trained and got driver’s license

(2) Operator should wear safe protective shoes,cap,costume in his operation

(3) Pay attention to the performance and working conditions of mechanics,hydraulic,electrical and MOSFET governor when operating

(4) Switch on the power,turn on the key,select the position of direction switch,roll the steering wheel to see if the truck is in order,step down the governor pedal slowly,keeping a proper starting acceleration

(5) Check the voltage meter when the truck is in working,if the value stated in the meter is less than 41V（72V）,stop working immediately,charge the battery or change another fully charged battery

(6) When conveying,the load should not exceed the rated capacity.The separation and position of forks should be appropriate,insert the forks absolutely downside the load,make the load uniformly distributed on the forks;to prevent load from deviation

(7) When the distance between the load’ gravity center and yoke is equal or less than 500mm.The maximum load capacity should be the rated capacity,and when the distance between the load’ gravity center and yoke is more than 500mm;the maximum load capacity should be less than the rated capacity

(8) When forks is bearing load,tilt backwards mast mostly,the yoke should always contact with load;lift forks upto 200mm high from ground before driving

(9) No standing under forks,no standing on forks when lifting

(10) The starting speed should not be too fast when starting to lift and lower the load

(11) No operation of truck and it’s additions without sitting on the driver’s seat

(12) Push handle immediately to middle position when the mast has tilted forward or backward to the extreme position

(13) No driving or turning when the mast is lifting

(14) When travelling,pay attention to passers by,obstacles,irregular road and the clearance of upper side of forklift

(15) Be careful of travelling on slope,when the angle of slope is more than10%,travel forward upslope and travel backward downslope. no turning on slope,no loading or unloading when travelling downslope

（16）Reduce speed when turning on the damp or slick road,take special care and drive slowly when travelling on dock or on temporary board

(17) Operating high lift range truck of which the lifting height is more than 3m,pay attention to the dropping of the load,and take measures to prevent it when necessary

(18) Don’t convey unfastened or loosely stacked load,be caref when conveying large-size load

(19) When travelling with load,avoid emergency brake

(20) When leaving the truck,lower the forks to ground;push lever to free position,switch off power,when parking on the slope,pull tight the brake apparatus and plug the wheels with wedge if the parking time is long

(21) The protection valves on multiway valve and on steering device are already regulated,so the users shouldn’t regulate randomly when using to prevent that the excessively high oil pressure leads to the damage of the whole hydraulic system and the burnout of the electric motor

(22) Charge the tyres according to the pressure value stated in “tire pressure” indication

(23) Treat the operation of non-load truck with additional apparatus as the operation load truck

## 5. Lithium Battery charging

(1) In the first time of charging or boost charging of battery,act strictly according to the rules stated in battery specification

(2) When the truck is in working,and when the battery voltage drops to 72V or the meter alarms,stop working immediately,charge the battery or change another fully charged battery

(3) Charge the battery at once after use of the truck,the storage period should be less than 24h;in order not to damage the battery,prevent under charging or over charging of the battery

# Chapter two The main performance parameters of forklift truck

## Ⅰ.The truck’s outline dimension and performance parameters.

### 1. The truck’s outline dimension  see figure 1-1

Figure 1-1 outline

### 2.Technical data

2.1FE4P25-35Q Technical data（list 1-1）

| Model number | FE4P25Q | FE4P28Q | FE4P30Q | FE4P35Q |
| --- | --- | --- | --- | --- |
| Drive mode: | Electromotion |
| Operation mode: | Seat-driving pattern |
| Rated capacity Q(kg) | 2500 | 2800 | 3000 | 3500 |
| Load center distance C(mm) | 500 |
| Load distance x(mm) | 478 | 483 | 487 | 492 |
| Wheelbase y(mm) | 1620 | 1700 | 1800 | 1800 |
| Service weight including battery kg | 1620 | 1700 | 4070 | 4480 |
| Axle loading,laden front/rear kg | 3600 | 3860 | 6390/680 | 7140/840 |
| Axle loading,unladen front/rear kg | 5500/600 | 6010/650 | 1750/2320 | 1960/2520 |
| Tyres size,front | 7.00-12-12PR | 7.00-12-16PR | 28×9-15-14PR | 28×9-15-14PR |
| Tyres size,rear | 6.00-9-10PR | 6.00-9-12PR | 6.50-10-10PR | 6.50-10-10PR |
| Track width,front b10(mm) | 973 | 973 | 1004 | 1004 |
| Track width,rear b11(mm) | 982 | 982 | 982 | 982 |
| Mask/fork carriage tilt foreward/backward α/β(°) | 6/10 | 6/10 | 6/10 | 6/10 |
| Lowered mast height h1(mm) | 2070 | 2070 | 2070 | 2185 |
| Freelift height h2(mm) | 135 | 135 | 135 | 140 |
| Lift height h3(mm) | 3000 | 3000 | 3000 | 3000 |
| Extended mast height h4(mm) | 4045 | 4045 | 4115 | 4115 |
| Overhead load guard height h6(mm) | 2150 | 2150 | 2150 | 2150 |
| Seat height h7(mm) | 1130 | 1130 | 1130 | 1130 |
| Traction pin height h10(mm) | 580 | 580 | 580 | 580 |
| Overall length l1(mm) | 3568 | 3663 | 3673 | 3678 |
| Length to face of forks l2(mm) | 2498 | 2593 | 2603 | 2608 |
| Overall width b1(mm) | 1150 | 1150 | 1226 | 1226 |
| Fork dimensions s/e/l(mm) | 40/120/1070 | 45/125/1070 | 45/125/1070 | 50/125/1070 |
| Fork carriage width b3(mm) | 3849 | 3949 | 1100 | 1100 |
| Ground distance,centre of wheelbase m2(mm) | 3997 | 4097 | 150 | 150 |
| Turning radius Wa(mm) | 2200 | 2300 | 2350 | 2350 |
| Travel speed,laden/unladen km/h | 11/12 | 10/11 | 11/12 | 10/11 |
| Lift speed,laden/unladen m/s | 0.26/0.34 | 0.25/0.33 | 0.26/0.34 | 0.25/0.34 |
| lowering speed,laden/unladen m/s | ＜0.6 |
| Drawbar pull,laden/unladen S2 5 minute % | 15/15 | 15/15 | 15/15 | 13/15 |
| Drive motor rating S2 60min kw | 11 | 11 | 11 | 11 |
| lift motor rating S3 15% kw | 16 | 16 | 16 | 16 |
| battery voltage,nominal capacity K5 v/A.h | 80/200 80/300/400 | 80/200 80/300/400 |
| battery weight kg | 210 | 210 |
| working pressure of attachments MPa | 17.5 |
| oil volume for attachment l/m | 36 |

（list 1-1）

# Chapter Three Operation,use and safety for forklift

## Ⅰ.Driving and operation

There are some information for operating normally as below and it favor you about good running performance, using safely, running economically.

### 1. Usage of new vehicle

·All of the parking parts from the new vehicle should be reclaimed according to the establishment of local government.

·In order to insure the new vehicle can work normally, Make a trial run of it before use it.

The life-span of vehicle depends on how you begin to use your new forklift. At initial 200 hours running, please to notice as follow.

·Whatever season, you have to run machine warmly before operating.

·Do maintenance better in normally.

·Do not abuse machine and unreason using.

### 2. Connection between load and stability

Under load curve, forklift take front wheel for pivot to keep balance of vehicle and load on fork, please pay attention to load centre and load capacity to keep vehicle stable.

· If exceed load curve, rear wheel should be uplifted and be in danger, forklift should be overturned to lead severe injury. Saying as below figure, load close to fork prong is the same effect as increase weight. As in such condition, load shall be decrease.

### 3. Load center and load curve

Load centre means the distance between front end surface of fork and cargo cg. Said figure of load curve show you relation of 2t forklift load centre and permitted load. figure of load curve is adhibited on vehicle, if figure damaged, to renew it in time.

·If forklift is equipped disposal accessaries such as side-move device, scraper bucket or rotating fork, its permited load is less than normal truck(no any accessaries), the reason as follow:

(1) Subtract load from rated load, its weight equal to weight of accessaries.

(2)Because accessaries length lead load centre to move forward, rated load is also decrease.

Accessaries equipped lead load centre moving forward, this phenomena is called “Load centre loss”.

Do not load exceeding the rated load shown by figure of load curve pasted on vehicle or accessaries.

### 4. Forklift stability

There are regulations in ISO or other standard about forklift stability, but said regulation is not applicable for all of running condition, forklift stability vary on different running condition.

Maximum stability is assured under below condition:

(1) Level and firm ground.

(2) Running under standard load or unloaded condition.

Standard no-load state: Fork or other bearing accessaries lie 30cm upto ground,tilting mast backward enough without load.

Standard load condition:Fork or other loading accessaries lift up about 30cm from ground,rated load on standard load centre, mast tilting backward to max.angle.

·When loading,keep min.tilting angle forward or backward as can as possible, do not tilting forward unless load fixed on load backrest or rigidity loading goods frame, or low lift height.

### 5. Transporting and loading for forklift

(1) Transportation of forklift

·Transporting with truck,Wedge forklift wheel or tighten forklift by rope to prevent it moving during transportation.

·Pay attention to obey regulation of full-length, full-width, full-height of forklift during transportation on traffic road.

(2) Loading and unloading for forklift

·Please use gangplank with enough length, width and intensity.

·Brake lorry firmly and wedge wheel.

·Gangplank shall be fixed on middle of carriage firmly, no greese on gangplank.

·Both height of left and right gangplank shall be same.

·Do not turn or transverse move during operating on gangplank.

·When loading on lorry, in order to let forklift board on simultaneously, please backing lorry slowly.

### 6. Preparation before driving

(1) Check position of direction switch handle⑤,and push it to neutral position(N).

(2) Turn on ignition key

Catch hold of handle of steering wheel,then turn on ignition key and keep it at “ON”position.

·Even after ignition key is turned to “ON”position,1 second is needed between brake circuit starting to work and starting to move.

·If gear shift lever is in forwardposition“F” or backwardposition“R”,before turn ignition key to“on”position,push gear shift lever to neutral position“N”

·Do notice that if step down accelerating paddle suddenly,vehicle will probably accelerate suddenly.

(3) Tilting backward of mast

Pull backward lifting handle to lift fork

150-200mm upto ground,and pull backward tilting handle to tilt mast backward.

(4) Operation of direction switch handle⑤

Direction switch handle decide travelling direction（forward-backward）

Forward F:push forward direction switch handle

Backward R:pull backward direction switch handle

(5) Loosen parking brake handle

Step down brake paddle

Let go parking brake handle forward entirely,catch hold of steering wheel with left hand,put right hand lightly on steering wheel too.

### 7. Steer

(1) Starting up

Move food away from brake paddle and step down accelerating paddle slowly,then,the vehicle will start to move.

Acceleration rate is decided by how much accelerating paddle is stepped down.

·Do not startup or brake suddenly to prevent cargo falling down .

(2) Speed slow down

Release accelerator slowly. If necessary, step brake pedal down. Except emergency brake, release accelerator to make slow down slowly until parking. If even release accelerator suddenly, emergency brake is also impossible. When emergency situation, step brake pedal down to make emergency brake.

·Please slow down if situation as follow:

(a) urning at crossing.

(b) Closing to cargo or pallet.

(c) Closing to goods pile.

(d) Traviling through narrow chunnel.

(e) Ground/Road surface is bad.

· When backing forklift you have to look at rear direction to be sure condition is safe. It is dangerous when backing forklift depending only on rearview mirrow.

(3) Turning

It is not same as car, forklift depend on rear wheel to turn. When turning you shall be slow down and be careful for tail swing of forklift when operating steering wheel.

·During turning, when turning radius is small, the fast speed the forklift is, the more possibility the forklift overturn. Be careful for this situation.

(4) Traveling and lifting simultaneously (Inching operation)

(a) Traveling first, let fork prong be close to goods about 3—5m distance.

(b) Step brake pedal down perfectly.(standstill)

(c) Step accelerator down to be in optimum speed.

(d) Operating lift and lowering handle to operate fork to be lifting operation.

· Traveling and lifting simultaneously (Inching operation) is a professional work to ask forskilled operator. Be definite to know well the shape and cg of goods to identify the vehicle stability, make a slow lifting and lowering performance of the vehicle,and please be careful in operation.

·Tilting fork to operate when fork is at a much height is very dangerous , except for fork’s in and out operation , please do not operate the vehicle on the load stage.

·In order to reduce the danger of tilting fork to operate when fork is at a much height,make lifting operation when the vehicle is very close to load stage.

### 8. Parking and temporary parking

·Parking safely

·Parking place shall be broad and level as much as possible.

·When unladed forklift have to park on ramp, please make mast face downward and block wheel by wedge.

·Parking vehicle outside workplace or qualified place.

·If necessary, to use signs or signal light.

·Parking on firm and level ground.

·If fork can not lower because of fault, hang cloth on fork prong forward dead corner.

·Pay attention for road surface slide or cave in.

·To lower fork after parking perfectly, it is very dangerous to lower fork during traveling.

·Do not jump off vehicle.

·When get off forklift, you have to face vehicle and take favour of footboard.

·Slow down first and step brake pedal down and standstill and put gearshift on “N”.

·Parking vehicle at place where is

convenient to other vehicle and operating as follow:

(a) Pull backward the parking brake handle enough to its position,actuate the parking brake.

(b) Let fork lower to make it touch ground.

(c) Turn ignition key to“off”position.

(d) Take off key and keep it carefully.

(e) Be careful to get on or get off vehicle.

(f) Parking forklift

·When get off forklift, pull brake handle up and to tilt mast forward. Lower fork on ground. When parking on ramp, block forklift by wedge.

·When leaving forklift, take ignition key

### 9. Usage of battery

(1) Charging battery

To choose right charger according to instruction of operating manual.

(a) Keep liquid on normal level.

·Keep liquid level on normal situation to prevent battery from being over-hot or being burn out.

·If electrolyte is not enough, the life-span of battery will be shorten

(b) Infuse distill water.

(c) Do not overcharge.

(d) Charging place shall be ventilated enough.

·Battery charging shall be at ventilated and dry place.

(e) Open bettery cover.

·There is hydrogen to be geverated when charging,so and please open bettery cover.

(f) Check terminal, cable and connector.

·Before charging, check connector and cable to ensure there is no injury

·Not charging under the situations as follow:

—Connector terminal has been injuried.

—There are rust and abrasion in Turminal and cable.

These situations will lead spark to burn and to explode.

(g) Charge after turning off ignition key.

(h) Check proportion

Before charging, check each cell for electrolyte proportion to detect for abnormal condition to prevent certain accident happen.

(i) When pulling out or insert power connector, hold connector or handle not the cable.

·Do not pull out cable.

·If cable and connector failure, please inform manufacturer to replace by new one.

(j) Break up charging procedure

·According to 《operation and maintenance manual》of the used charger to break charging procedure.

·Do not pull out charger plug during charging, otherwise there will be spark take place to lead to danger.

(2) Replace bettery

When forklift has been used continuously for a working period and the battery has entirely excharged,replace the battery with another fully charged one and charge the battery been replaced.

·In replacing, to be sure that new battery mates with forklift well, otherwise there will be dangerous to shorten lifespan of forklift or overturn during traveling.

·Replacement of battery shall be done on level table.

According to the steps as below to replace battery:

·When using another forklift as hoisting equipment to lift battery, you shall choose a proper lifting tool(accessary).

·Only qualified person can operate battery.

(a) Pull out plug of battery.

(b) Open upper cover of battery.

Use gas spring or other methods to ensure block upper cover of battery to avoid cover fall down to injure human or bodywork.

(c) When hoisting battery out forklift, be careful for touching steering wheel or other forklift parts.

(d) After finish installation of battery, connect and fasten the battery pin.

(e) Close upper cover of battery.

· When close upper cover of battery, be careful  to injure your finger.

·During hoisting battery, be careful to prevent swing of battery box to injure bodywork.

### 10．Stacking

·Check the following items before operation:

(a) Be sure that there are no falling of load and damaging of load in loading region.

(b) Be sure that there is no goods or pile

possible leading to unsafety

Stack as follows:

(1) Slow down when getting close to goods.

(2) Parking in front of goods.

(3) Check the safety of goods area.

(4) Adjust the position of vehicle until it lies in front of goods

(5) Make Mast vertically ,lift fork up more than the height of goods.

(6) Check goods’location and park the vehicle to optimum position.

(7) Ensure that the load higher than the stacked goods and lower fork slowly and place load correctly and safely.

·Before load placed on shelves or bracket:

(a) Lower load until fork no longer carry any load.

(b) Backing forklift for distance of 1／4 length of

fork.

(c) Lift fork 50—100mm up and drive forklift forward for stacking to be optimum.

(8) Look at rear space, backing forklift in order to avoid impact between fork and pallet or goods.

(9) Ensure fork prong to be off goods or pallet, lower fork to avail driving.(from ground 150—200mm)

### 11．Unstacking

Unstack referring to the procedure as below

(1) Slow down when close to goods.

(2) Park in front of goods(30cm between goods and fork prong)

(3) Adjust the vehicle position in front of goods

(4) Be sure that there is no overloading.

(5) Adjust the Mast upright to ground.

(6) Observe the vehicle position and move it forward until the fork inserts the pallet completely

·When it is difficult to insert the fork completely into pallet：

(a) Inserting 3／4 length of fork and lift pallet little more (50－100mm), then pull fork out pallet 100-200mm,

then lower pallet.

(b) Insert fork into pallet completely.

(7) After fork insert pallet, lift pallet (50-100mm) up.

(8) Look at ambient spacy to move forklift backward to lower load.

(9) Lower load at the height of 150-200mm from ground.

(10) Tilt backward the mast to ensure the stability of goods.

(11) Transport the goods to destination

### 12 Deposit

(1) Before diposit

Before forklift deposits,clean it thoroughly, check up as following:

(a) If necessary, clean grease and oil of bodywork by cloth and water.

(b) When cleaning, check the vehicle entirely especially for hollow or damage of bodywork, if tires punctured, and if there is any nail or stone in tire surface groove.

(c) Check for leakage.

(d) If necessary, infuse greese.

(e) Check wheel hub nut and joint face between piston rod and piston for loose, check piston rod surface for injury.

(f) Check mast roller for rotation stability.

(g) Actuate lift cylinder to its max. height to let cylinder be full of liquid.

·As long as there is any failure or malfunction or unsafe factor of forklift to be

known,report to related person and stop using forklift until repaired.

(2) Daily deposite

(a) Parking forklift on appointed place and block wheel by wedge.

(b) Put shift gear on neutral and actuate parking brake.

(c) Take off ignition key and keep it in safe area.

(3) Long time deposite.

Based on daily deposit,please make check and maintenance according to the follow items.

(a) Considering the raining season, park the  vehicle on high and rigid ground.

(b) Unload battery from forklift.even indoor parking,if the place is muggy,dry and shade-cool are necessary fo the battery depositing. Charge the battery once a month.

(c) Rub anticonosive oil on bared surface of piston rod and shaft ect.

(d) Cover parts prevent raining and wet.

(e) Startup vehicle at least once a month, install battery, clean the grease on piston and shaft, startup engine and preheating, make vehicle move forward and backward slowly, meanwhile operating hydraulic control for several times.

(f) In summer, do not park forklift on floppy furface such as asphalt ground.

(4) Operation after long time deposit.

(a) Take off dampproof cover.

(b) Cleaning pickling oil from bared parts.

(c) Cleaning impurity and water of hydraulic tank.

(d) Install full charged battery on forklift andconnect it.

(e) Check carefully before startup.

## Ⅱ.Using instruction of operating devices

### 1. Components,schematic diagram for operating devices（see following figure）

| 1.mast | 2. lifting oil cylinder | 3. Lifting chain |
| --- | --- | --- |
| 4. load-backrest | 5.fork | 6.front wheel |
| 7. parking braking | 8. service braking sytem | 9．accelerator |
| 10. charge Jack | 11.hood | 12.real wheel |
| 13. counterweight | 14.rear combination lamp | 15. overhead guard |
| 16.seat | 17. operating lever | 18. steering wheel |
| 19. Headlights and turn signals |  |  |

### 2. Instrument unit

see figure 2.4 Electrical system（ page 30）。

### 3. Switches

（1）Emergency stop button

When emergency, press red mushroom-head button down to cut off power to stop function of traveling, turning, lifting. To resume the function,rotate the botton according to the arrowhead indication.

(2)Key switch

key can turn on or turn off controlling power

Turn off (0FF): In this position,power is cut off and key can be inserted and pulled out

Turn on (0N): Turn forward from off position,switch is turned on,forklift starts up.

·Do not turn on ignition key and step accelerator down simultaneously.

·Take off key to prevent unqualified operating when get off forklift.

·Take off key when charging or parking to prevent unqualified operating.

（3）Switch unit

Switch unit is combined by direction switch,steering switch and big and small light switch.

1- direction switch	      2- steering switch         3- big and small light switch

Direction switch controls travelling direction and delivers signal to instrument to display. Push handle forward,vehicle travel forward,and pull handle backward,vehicle travel backward. Neutral position is vacancy. When handle is on backward,back-up light and caution light will open,back buzzer has sound.

Steering lisht shows rotation direction of forklift,when handle is on turning position,steering light will blink.

| push forward | left steering light is bright |
| --- | --- |
| middle | neutral |
| pull backward | right steering light is bright |

Big and small lights switch control relevant lights. Small light will open when rotate to the first gear,both big and small lights will open when rotate to the second gear.

| gear light | OFF | first gear | second gear |
| --- | --- | --- | --- |
| width light | × | ○ | ○ |
| tail light | × | ○ | ○ |
| fore light | × | × | ○ |

○: lightening  ×: blanking

（4）Rear big light switch

Tail light switch is a single gear which controls on&off of the light. Pull switch up, light open; push down, light off.

### 4. Control

- Ssteering wheel①and steering wheel handlebar②

Steering wheel operation is traditional: steering wheel turn right, vehicle move right; steering wheel turn left,vehicle move left.There is steering wheel at backside of forklift to make backside of forklift swing toward outside when turning.

When turning, catch steering wheel by left hand and right hand on steering wheel or control handle of multiway valve.

Both hydraulic steering system and steering wheel tilting device are standard equipment of forklift.

·According to driver seat to adjust steering wheel to optimum angle.

·Lock steering pipe by tilting handle after adjusting steering wheel tilting angle.

(2) Horn button④

Push down rubber cover located in the center of steering wheel to make a buzzing sound. Even when ignition key is turned off,the horn can also sound.

(3) Direction switch handle⑤

Indicate travelling direction

Travel forward (F): Push forward handle and step down accelerating paddle

Travel backward (R): Pull backward handle and step down accelerating paddle

When parking forklift,direction switch handle should be put in neutral position(N).

(4) Parking brake handle⑥

In order to prevent forklift from moving,when park forklift,pull up entirely parking brake handle.

It is necessary to push parking brake handle to end before driving.

·When operating the parking barke handle,step down the parking paddle.

(5) Brake paddle⑦and accelerating paddle⑧

·Do not step accelerator pedal suddenly to prevent the vehicle from starting or accelerating suddenly.

·Ensure your foot remove from accelerator pedal when step brake pedal down.

From left to right,there are brake paddle⑦ and accelerating paddle⑧ in turn.

Step down accelerating paddle slowly,forklift speed is decided by stepped angle of accelerating paddle.

(6) Lifting handle⑨

Pull backward lifting handle,fork lifts,and push forward lifting handle,fork lowers.lifting and lowering speed depend on tilting angle of handle,the larger the angle,the faster the speed is.

·Lifting operation cann’t be made,if push or pull lifting handle when turn on ignition key.

·Don’t lower fork suddenly or stop suddenly when lowering fork.

(7) Tilting handle⑩

Pull backward tilting handle,mast tilts backward；push forward tilting handle,mast tilts forward.Tilting speed is decided by tilting angle of hande,the larger the angle is,the faster the speed is

·When turn ignition key on, push or pull tilting handle, you can not tilt mast.

### 5. Truck body

(1) Seat

Make you fit to drive seat by adjust operating handle.

Lock will be released after pull the handle up. you can move seat to and fro gently. To be sure seat locked after adjusting.

Seat adjusting range To and fro is 120mm. When traveling on dry cement road, driver is given a perpendicular acceleration is 2.130m/s2-2.237m/s, integrative acceleration is

2.252m/s-2.356m/s.

(2) Roof guard

·Roof guard protect you from falling down of goods. Its top is a fence-type shape, the space between two bars is 150mm, so, if goods size is less than 150×150mm, you have to adopt another measure to protect youself from danger of falling down of weights. Abnormal installation of roof grard or no roof guard or changing roof guard shall lead terrible accident.

(3) Goods rest

·Goods rest is an important device to protect operator from being impacted when cargo slides toward operator. Loose installation,usage after dismantling and usage after modification are all dangerous.

(4) Traction rod

Only in the following situation shall be possible to use traction rod.

·To escape from the trouble of being not able to travel(for example wheel trapped in ditch)

·Forklift need to be loaded on or be unloaded from lorry.

·No using for towing or to be towed operation absolutely.

(5) Fitting pin for fork

Fork fitting pin lock fork on certain position. When need to regulate clearance of fork, pull pin out up, rotate pin l／4 circle to make fork at position required. Regulation of clearance of fork depend on goods need to be loaded .

·According to principle of goods gravity centre shall be on centre of vehicle, we have to regulate space of forks for equal distance either left and right.after regulated, to fixup fork by fitting pin firmly.

· When adjust space of fork, lean against your body on goods rest, after standing stably,push fork by your foot. Do not regulate by your hands absolutely.

(6) Foot pedal and armrest

There are foot pedal on each side of forklift, armrest located on left front brace of roof grard, when get on or get off,please use foot pedal and armrest to ensure your safety.

(7) Lamps

There are head light and front light assembled on the head of vehicle direction indicator lamp, parking light, width light). Also there are back light assembled on backside of vehicle which consists of tail light, turning light, brake light, parking light, back light and flasher.

·Identify the working status of lamps,

Replace and repair lamps immediately if lamp burning out, lamp shield injury or dirty.

(8) Rear view mirror

Rear view mirror locates in right of roofguard front beam.

·Keep rearview mirror surface cleanness.

·Regulate rearview mirror for good position in favor of good sight of driver.

(9) Battery plug

Battery plug is used to join or cut off power, in normal situation, it should always be connected.

·If checking electrical parts of inside location, please cut off power to prevent danger.

·Even if ignition key on “0FF”, main circuit Still has voltage.if you want to switch off power,it is necessary to pull out this connector.

·Do not pull out plug of battery during Driving unless emergency, because it can lead steering malfunction.

## Ⅲ.Safety issues

Safety is your business and responsibility. This section describes the typical forklift often used in the basic safety regulations and warnings, but also applies to the door frame with special specifications.

### 1. Operation place and working environment

(1) Ground conditions

The operation place of forklift should be ground with flat and firm surface,a good ventilation is needed.

Forklift's performance depends on the situation of the ground; running speed should be adjusted appropriately in ramps or rough pavement to be especially careful when driving. Driving on a ramp or rough roads will speed up the forklift tire wear and increased noise.

(2) Work environment

Forklift use ambient temperature should be 5 ° C ~ 40 ° C, the ambient humidity should less than 80%.

(3) Weather condition

When it’s rainy,snowy,foggy or windy,to assess the safety before use forklift,the best is not to use for out door work,if must,driving and operation should be more carefully.

### 2. Safety rules

Only qualified people who has been trained and

has driver license can operate the forklift!

Forbid to drive on the highway!

Vigilant: injuries, the ambulance!

Do not change parts on forklift arbitrary           Read the instruction manual carefully before without permission.                             driving!

Turn off the engine before maintenance!      Understand traffic regulations

Before use, please check on the truck!          Do not move the overhead guard!

To keep driver’s cap clean!                        Do not drive an unsafe forklift!

Drivers should have a healthy body!          Be sure your truck is safe!

Work in specified area                      Do not drive a damaged truck!

Hold tightly when get on the truck!            Start forklift correctly!

Adjust seat before driving!                     Make sure your forklift is in safe operating

condition!

Appropriate fasten seat belts!             Always pay attention to the height of work place!

Turn on lights in dark area!                 Do not put arm and body outside of the

overhead guard during work!

Avoid driving on soft ground, only           Keep body under the guards!

allowed to run on solid and flat ground.

Avoid eccentric loading!                  Pay attention to encounter item by front

fork when loading!

Check fork pin position!                     Note the security of the work region!

Do not run on smooth or slippery ground!       Note the horizontal driving stability of the

truck when it is un-load!

Be especially careful when handling long      Forbid handling people!

or wide cargo!

If can not see the front when turning,           Use appropriate pallets or sleeper when

please whistle and drive slowly.                handling small objects!

Do not chase each other through the traffic!    Not allowed to stand on the goods!

Not allowed to gaze around while driving!   Do not use the forklift to do stunt!

when goods is so high to keep out line       Should obey the traffic rules and all

of sight,drive backward or forward under     warnings and signs!

direction of others

when loading,travel forward in upgrade        Pay attention to the steep uphill slopes

and backward in downgrade                  and goods lifting height!

When no-load,travel backward in upgrade      Note using brake when start truck on

and travel forward in downgrade!              the slopes!

Not turn when driving on a slope!           People or things moving on road should

be warned by whistle!

Be careful to crush people or goods            Operators are not allowed to close when the

when turning!                                truck is working!

While turning a high speed can cause        People are not allowed to start in work place!

accident because of unstable center of gravity!

Notice the change of rated load weight     Pay attention to the area where forklift

before use forklift.                       is driven!

Use the fork correctly when loading!             Slow down when loading!

Do not move the truck when there is         It is forbidden to stand or walk under

someone in front of the truck!               the elevatory fork!

Do not load the goods which is higher        Please bind the goods which is difficult

than the goods rest.                        to fix before load!

Do not carry the goods from forklift by       Do not let people to carry the goods have

manpower!                               been damaged!

Do not misuse the fork!                     Be careful when load the container!

Do not pick up people!                      Do not misuse forklift!

Do not extend any part of body outside       Drive the truck smoothly to avoid sudden

when driving!                              acceleration and deceleration!

Must use special equipment to lift people      Do not overload!

safely to lift people safely to work at height!

Do not lift when there is excessive wind!    Not allowed to work in explosive environments!

The faulty trucks should be put into the        park the forklift to the indicated area!

indicated area!

Do not park the forklift on the slope!       When the forklift is not in use,please do

the follow.

— Brake

— Put direction pole in neutral position.

— Lower the fork to the ground

— Frame forward tilt.

— Take off the key

### 3. Move the truck

Forbid hoisting from the top!                   Forbid hoisting on the frame!

Hoisting the forklift correctly!

Hoisting the forklift

·Tie firmly steel cable on two terminal holes of outer mast beam and on counterweight hoisting hook,then,hoist forklift with hoisting device.the side of steel cable connecting to counterweight should go through notch of roofguard without exerting pressure on roofguard.

·When lifting the truck, be sure not to wire rope and overhead guard around together.

·Wire rope and lifting equipment to be very strong, enough to secure bearing fork lift, because the truck is extremely heavy.

·Do not use the cab (overhead guard) to hoist the forklift.

·Forklift upgrade, do not enter the truck underneath.

### 4. How to avoid overturning,how to protect yourself

Prohibit forward tilt to enhance loading,     Prohibit lifting goods tipsily!

so as to avoid tipping!

Prohibit eccentric loading of goods!          To avoid driving on slippery roads!

When the truck is not in the horizontal     Prohibit crossing the obstacle such astrench,

position, do not load or unload!           mound and railway!

When moving, the distance between fork and  whether load or no-load,don’t turn in a high

ground should less than 150mm to 200mm!     speed or in a large radian !

when no-load fork is lifted,please turn with        Be sure to fasten seat belts!

a narrow range.

Do not jump in the event of forklift rollover!     Please wear helmets when driving!

·It is more safe to stay under the protection of seat belt than jump down the truck. If the forklift began to tip over:

1. Tap foot and clench the steering wheel tightly.

2. Do not jump.

3. The body bend to the opposite direction of the rollover.

4. Forward the body.

### 5. Safety problem in Maintenance

(1)  Maintenance location

·Designated areas should be available to service providers and adequate equipment and security facilities.

·The site should be level ground.

·The site should be well ventilated.

·The site should have fire-fighting equipment.

(2) Precautions before maintenance

·No smoking

·Wear all protective equipment (helmets, shoes, glasses, gloves and boots), and suitable clothing.

·Wipe out the oil in time.

·When add lubricating oil, you should clean out dirty oil or dust with a brush or cloth, then add oil.

·In addition to the needs of some cases, should turn off the key switch and pull the battery plug out.

·Lower the fork to ground when maintaining.

·Clean the electrical components with compressed air.

(3) Matters need attention.

·You should be careful not to put your feet under the decensive fork, do not be tripped over by fork.

·When fork is lifted,place cushion block or other object under inner mast to prevent fork and mast from falling down suddenly.

·You should be careful when you open and close the noseplate and cover plate of battery.

·When you can not finish your work in one time,please make mark and go on next time.

·Use the right tools, do not use makeshift tools.

·Because of high pressure hydraulic circuit, do not carry out maintenance work before reducing the internal pressure oil-way.

·When shocked by high-voltage,search for medical treatment immediately.

·Do not use the door frame assembly as a ladder.

·Strictly forbidden to put your hands,feet and body between frame and door frame assembly.

(4) Inspect and replace tires.

·Assembly and disassembly of tires must be operated by professionals.

·High-pressure air should be carried by professional.

·Wear goggles when using the compressed air.

·When disassemble tires, do not loose rim junction bolts and nuts, there is high-pressure gas inside the tire, bolts, nuts and rims loose cause very dangerous situation.

·Junction disassembly rim bolts and nuts, the tire must be exhausted within the high pressure gas, and carried out special tools.

(5) Use jack (replacement of tyres)

·When lift the forklift truck with a jack, do not bore into the botton of forklift.

· Before lift the forklift truck with a jack, ensure there is no person or load on the truck.

·When forklift is of ground,stop using jack and put pad under it to prevent it from falling down

·Before lift forklift with jack,affirm there is nobody and no load on it

(6) Emission (electrolytic liquid, oil, etc.) requirement.

·Forklift scrapped parts (plastic parts, electrical components, etc.), liquid (hydraulic oil, brake fluid, etc.) should be recycled according to local government stipulation,do not dispose them at will.

### 6. Safety problem in battery usage

(1) No smoking

·Batteries produce hydrogen gas. Short circuit will produce sparks when lit cigarette near the battery, it will cause an explosion and fire.

(2) Avoid electrical attack

·Battery with high voltage, when the installation and maintenance, do not touch the battery conductor, which can cause serious burns.

(3) Correct link

·When the battery charging, the positive and negative can not be reversed, otherwise it will cause heat, fire, smoke or explosion.

(4) Do not put metal objects on the battery

·Do not let positive and negative contacts cause a short circuit by bolts or tools, which will result in injuries and explosions.

(5) Against excessive discharge

·Do not use forklift until it can not move, otherwise the battery life will be shortened. The batteries need charging up when the battery capacity warning light flashes continuously.

(6) Keep clean

·Keep the battery surface clean.

·Do not use dry cloth, chemical fiber cloth to clean the battery surface. Do not use polyethylene film covered battery.

·Static electricity can cause an explosion.

·Clean the top of the battery not covered with a moist cloth.

(7) Wear protective clothing

·When maintain the batteries, you should wear goggles, rubber gloves and rubber boots.

(8) Battery electrolyte is harmful

·Battery electrolyte is made of diluted sulfuric acid, be careful when handling.

·When electrolyte adhesion conglytination on eyes, skin and clothing, it will result in vision loss and burns.

(9) Emergency dealing methods

·When the accident occurred, deal according to the following methods of emergency treatment and contact a doctor immediately.

·Splash on the skin: wash with water for 10-15 minutes.

·Splash into the eyes: wash with water for 10-15 minutes.

·Contaminated for a large area：counteract(baking soda)electrolyte with dry soda or clean it out with water

·Swallowed: to drink plenty of water or milk.

·Spilled on clothing, immediately take off clothes.

(10) Close battery cover tightly.

·Cloth battery upper cover tightly to prevent electrolyte from leaking.

·Do not add too much electrolyte, electrolyte overflow will cause leakage.

(11) Waterproof

·Batteries can not be wet with rain or sea water, this will damage the battery or cause fire.

(12) Battery anomaly

·When the battery has the following situations, please contact our sales department:

·Battery stinks.

·Dirty of electrolyte.

·Electrolyte temperature becomes higher.

·Electrolyte reduces too quickly.

(13) Prohibit disassemble

·Do not drain the electrolyte from the battery.

·Do not split the battery.

·Do not repair the battery.

(14) Stored

·When the battery is not in use for a long time, it should be stored in well-ventilated place and difficult to fire.

(15) Disposal of waste batteries

·Disposal of waste batteries should contact our sales department.

# Chapter four Electrical system

Electrical system of FE4P25-35Q is powered by 80V battery set, Electrical system of FE4P30-35Q is powered by 80V battery set .traction power of the truck is powered by AC motor，lifting power is produced when AC motor is driving the oil pump to produce oil pressure. Lighting system is powered by battery 80V to 24V voltage.

### 1 Electric control assembly（Curtis）

(Figure4-1)

### 2 Electric control assembly（Inmotion）

(Figure4-2)

Forklift traction is AC variable-frequency motor, steering is AC variable-frequency motor controller, the dashboard display screen and AC drives adopes products from Curtis or Inmotion, The adopted AC variable-frequency motor is high efficient, durable and maintenance free, basically because it has no DC motor commutator (commutator can limit the acceleration performance of truck, especially in high speed situation, it will limit braking torque), so its accelerating ability is faster. Controller is used for ecectric truck which use CANopen protocol controller for communication, through its analog and digital I/O and communications devices, it is very suitable for management of forklift movement, I/O operation, control and information display, it can discharge of battery monitoring, with all kinds of protection function. Dashboard display can show many data, undertake factory or user setting, can input multiple functions such as user commands.

Electrical principle chat—Curtis(Figure4-3)

（Figure4-3）

Electrical principle chat—Inmotion(Figure4-4)

（Figure4-4）

### 2 Main functions and settings

Safe and high efficient working performance and complete operating performance of electric forklift can be achieved by setting correctly each motor technique data and control technique data and function value of controller.

1. The creeping speed of electric forklift can be set,the electric forklift work for a long time under a low speed,through creeping speed seting function of controller.

2、Acceleration can be set. Acceleration is the sense of softness or hardness of accelerating padal when operating electric forklift. By setting rate of rate,forklift can meet the need of accelerating operation under different working condition.

3、Plug braking and regenerative braking. In the course of travelling,there appears,when reversing direction rod,plug brake signal which,through the controlling of motor driver to pulling motor,presents a brake moment so as to brake the vehicle.The amount of brake power can be controlled by accelerating pedal. A proper setting of maximum brake power can ensure to brake electric forklift smoothly under different speed.Regenerative brake is,under the condition that the vehicle speed is higher than the rated value of accelerating pedal,generated by the controlling of controller. The brake power can transfer to electric power and present back to battery.Especially when the vehicle is coasting downwards slop,in order to properly reduce the speed,regenerative brake can be achieved by properly releasing the accelerating pedal.The presenting back of electric power to battery prolongs the one-charge-travelling distance of it.

4、Function of backward slip preventation on slope,when the vehicle is stopped on slope,it will slip downward the slop acceleratedly if hand brake or food brake pedal is released. The function of backward slip preventation can prevent the phenomenon of slipping downward acceleratedly and ensure that electric forklift slips downward uniformly with a low speed.

5、The maximum travelling speed can be set.The setting of the maximum travelling speed of electric forklift can prevent pulling motor from overloading caused by excessive vehicle speed.

6、Shut down static recovery,controlling device will be shut down if seat swith or ignition key is off..Only when the direction controlling rod is switched to neutral position can the vehicle be restarted.That is to say,if the driver leaves vehicle at any time and returns back to it,it is necessary to switch the direction controlling rod to neutral position to restart. This function can prevent unexpected insecurity. There is two seconds of time delay at the input end of seat switch,which allows seat switch can be off in trashing.

7、Safety protection function.When the power element in controller is damaged in vehicle travelling,the controller will cut off main contactor as quickly as possible.When the temperature ascending speed  of controller is too high,the controller will automatically limit the armature current of motor. And when the battery voltage is too low,the controller will stop working to keep safe.

8、There is self-diagnose function in pulling motor controller and oil pump motor controller.Once malfunction occurs in the working of controller,there will display malfunction code in indicating instrument,which will stop the controller from working to ensure the safety of operating system.

9、Display instrument will show battery power and the cumulative working hours.

### 3 Maintenance of circuit system

(1)、Check the contact wear condition; replace the contact if it’s worn and the contact should be checked every three months.

(2)、Check the pedal and tiller micro switch; Measuring the voltage drop at the ends of the micro switch, there is no resistance when the micro switch micro open closure should be without resistance, when released should have a clear voice.Check once every three months.

(3)、 Check the main circuit: battery- controller- connecting cable of the motor. To ensure that the cable insulation is good, the clamp circuit connection is fixed. Check once every three months.

(4)、Check the pedal mechanical movement to see whether the spring will deform, whether potentiometer spring can stretch out or draw back to the maximum level or setted levels.Check once every three months.

(5)、Check the contactor mechanical movement, the contactor should move freely without adhesion, mechanical movements of the contactor shall be inspected once every 3 months.

### 4 Combination instrument

Using new combination instrument, the main function is to realize auxiliary control and provide the vehicle display interface to the driver. It is composed of control circuit, the cumulative time counter (liquid crystal display), battery meter, fault code display and other circuit. Based on the current electric car demand, this instrument have new design in the control circuit and display form, which can provide drivers intuitive vehicle state information. This instrument has many advantages, such as compact structure, beautiful outline, high automatic degree and reliable quality.

Figure 4-5  CURTIS instrument

Figure 4-6  Inmotion  instrument

### 5 Failure analysis

1）Curtis  Controller fault table and diagnostics guide

| Code display on the programmer | Code display on the instrument | Troubleshoot | Fault cause |
| --- | --- | --- | --- |
| Controller Overcurrent | 1.2 | controllercurrentoverload | 1、motor outside U,V or Wconnection shour current 2、motor parameter mismatching 3、controller failure |
| Current Sensor Fault | 1.3 | Current sensor failure | 1，motor U、V、W truck circuit，lead to current leakage 2，controller failure |
| Precharge Failed | 1.4 | Precharge failure | 1，battery can’t chagge |
| Controller Severe Undertemp | 1.5 | Controller temperature too low | 1，The controller working environment is too harsh |
| Controller Severe Overtemp | 1.6 | Controller temperature too high | 1，The controller working environment is too harsh 2，truck overloaded 3，the controller is wrongly assembled |
| Severe Undervoltage | 1.7 | Voltage too low | 1， battery parameter is wrongly setted 2， non controller system power consumption 3， The battery impedance is too large 4， battery connection is disconnected 5，the fuse is disconnected, or main contactor is not connected |
| Severe Overvoltage | 1.8 | Voltage too high | 1，Battery parameter is wrongly setted 2，The battery impedance is too large 3，Regenerative braking when the battery connection is disconnected |
| Controller Overtemp Cutback | 2.2 | Controller temperature too high, as a result the performance is not good | 1, The controller working environment is too harsh 2，truck overloaded 3，the controller is wrongly assembled |
| Undervoltage Cutback | 2.3 | Voltage too low, as a result the performance is not good | 1， battery power is insufficient 2， Battery parameter is wrongly setted 3， non controller system power consumption 4， The battery impedance is too large 5， battery connection is disconnected 6， the fuse is disconnected, or main contactor is not connected |
| Overvoltage Cutback | 2.4 | Voltage too high, as a result the performance is not good | during the process of regenerative braking, regenerative braking current lead the battery voltage to rise 2， Battery parameter is wrongly setted 3， The battery impedance is too large 4， when regenerative braking |
| +5V Supply Failure | 2.5 | Controller output 5v, poer supply failre | 1， external load impedance is too low |
| Digital Out 6 Failure | 2.6 | Drive 6 output overcurrent | 1， external load impedance is too low |
| Digital Out 7 Overcurrent | 2.7 | Drive 7 output overcurrent | 1， external load impedance is too low |
| Motor Temp Hot Cutback | 2.8 | The motor is too hot, as a result the performance is not good | 1，The motor temperature reach or above the setted program alert temperature, lead the current output to reduce 2， motor temperature parameter is wrongly setted 3， If the motor has not used the temperature sensor, programming parameters “Tempcompensation”and“Temp cutback”must be setted“OFF”。 |
| Motor Temp Sensor Fault2.9 | 2.9 | Motor temperature sensor failure | 1， Motor temperature sensor is wrongly connecttedly 2， If the motor has not used the temperature sensor, parameter programming“MotorTemp Sensor Enable”must be setted“OFF” |
| Coil 1 Driver Open/Short | 3.1 | Drive 1 output linkng coil is open circuit or short circuit | 1， connected load is open circuit or short circuit 2， connecting pin is stained 3， wrong wiring |
| Main Open/Short | 3.1 | Main contactor coil is open circuit or short circuit | 1， connected load is open circuit or short circuit 2， connecting pin is stained 3， wrong wiring |
| Coil2 Driver Open/Short3.3 | 3.2 | Drive 2 output linkng coil is open circuit or short circuit | 1. connected load is open circuit or short circuit 2. connecting pin is stained 3. wrong wiring |
| EMBrake Open/Short | 3.2 | Electromagnetic brake coil is open circuit or short circuit | connected load is open circuit or short circuit 2， connecting pin is stained 3， wrong wiring |
| Coil3 Driver Open/Short | 3.3 | Drive 3 output linkng coil is open circuit or short circuit | 1，connected load is open circuit or short circuit 2， connecting pin is stained 3， wrong wiring |
| Coil4 Driver Open/Short | 3.4 | Drive 4 output linkng coil is open circuit or short circuit | 1，connected load is open circuit or short circuit 2， connecting pin is stained 3，wrong wiring |
| PD Open/Short | 3.5 | Proportional driving is open circuit or short circuit | 1， connected load is open circuit or short circuit 2， connecting pin is stained 3， wrong wiring |
| Encoder Fault | 3.6 | Encoder failure | 1，motor encoder is failure 2， wrong wiring |
| Motor Open | 3.7 | Motor is open corcuit | 1， motor phase 2， wrong wiring |
| Main Contactor Welded | 3.8 | Main contactor adhesions | 1， Main contactor contact welding 2， motor U or V disconnected or default phase 3，circuit that connecting B+ terminal will electricize the battery |
| Main Contactor Did Not Close | 3.9 | Main contactor is not closed | 1， main contactor is not closed 2，Main contactor pin is oxydic, melted, or not stable when connected 3， external device electricize the battery 4， fuse is disconnected |
| Throttle Wiper High | 4.1 | Accelerator output is high | 1，accelerator and potentiometer output voltage is too high |
| Throttle Wiper Low | 4.2 | Accelerator output is low | 1，accelerator and potentiometer output voltage is too low |
| Pot2 Wiper High | 4.3 | potentiometer 2 output is too high | 1，potentiometer 2 output voltage is too high |
| Pot2 Wiper Low | 4.4 | potentiometer 2 output is too low | 1，potentiometer 2 output voltage is too low |
| Pot Low Overcurrent | 4.5 | potentiometer current is too low | 1，potentiometer impedance is too low |
| EEPROM Failure | 4.6 | EEPROM failure | 1，EEPROM storage failure |
| HPD/Sequencing Fault | 4.7 | High pedal protection /operation order failure | 1，The key start, interlock, direction, and the accelerator input order is wrongly setted. 2， Wiring, switch key, interlock, direction, or accelerator input failure |
| Emer Rev HPD | 4.7 | Emergenvy reverse high pedal protection | 1，Emergency reverse operation is over, but the forward, reverse input and interlock of the accelerator are not resetted |
| Parameter Change Fault | 4.9 | Parameter change failure/wrong | 1，In order to ensure the safety of the truck, some specific parameter changes must come into force after the key switch is restarted |
| CAN Communications Fault | 5.1 |  |  |
| BMS PDO Timeout | 5.2 |  |  |
| BMS First Level Fault | 5.3 |  |  |
| BMS High temp fault | 5.4 |  |  |
| Safety belt operation sequence | 5.5 |  |  |
| Battery type mismatch | 5.7 | Connecting Lead Acid | Replacement of lithium batteries |
| Display Config Fault | 6.3 |  |  |
| BMS Overvoltage | 6.4 |  |  |
| BMS Undervoltage | 6.5 |  |  |
| BMS Low AH | 6.6 |  |  |
| BMS voltage differnce | 6.7 |  |  |
| VCL Run Time Error | 6.8 | VCL running time is wrong | 1，VCL code running time is overtime |
| External Supply Out of Range | 6.9 | Externial battery output is out og range | externial loading is between 5V and 12V , battery current is too big or too small 2， in the“inspection menu (CheckingMenu)”, parameter is wrong, such as “ExtSupply Max”,“Ext Supply Min” |
| OS General | 7.1 | Operation system failure | 1，internial controller failure |
| PDO Timeout | 7.2 | PDO overtime | 1，CAN PDO information reception time exceeds PDOtime limition |
| Stall Detected | 7.3 | Motor stalling | 1， Motor stalling 2， motor encoder failure 3， wrong connection 4， input motor encoder battery failure |
| Supervisor Fault | 7.7 | 1. The Supervisor has detected a mismatch in redundant readings. 2. Internal damage to Supervisor microprocessor. Switch inputs allowed to be within upper and lower thresholds for over over 100 milliseconds. | Set: Mismatched redundant readings; damaged Supervisor; illegal switch inputs. Clear: Check for noise or voltage drift in all switch inputs; check connections; cycle KSI. |

2）Inmotion Controller fault table and diagnostics guide

| Code display on the programmer | Code display on the instrument | Troubleshoot | Fault cause |
| --- | --- | --- | --- |
| 1 | 20 | Incorrect start Accelerator pedal switch active before key on | Release pedal switch |
| 2 | 21 | Incorrect start Forward switch or reverse switch active before key on | Turn off the direction switch |
| 3 | 22 | Forward switch and reverse switch active at the same time | Direction switch fault |
| 4 | 23 | Throttle analog value out of range | Throttle fault or analog need to be calibrated |
| 5 | 24 | Throttle analog fault |  |
| 6 | 31 | Traction controller CAN communication fault | Check CAN wire of controller and display |
| 7 | 32 | Battery voltage low | Need charge |
| 8 | 34 | CPU fault | Reset key |
| 9 | 36 | Incorrect start Tilt switch active before key on | Reset tilt switch |
| 10 | 37 | Incorrect start Side switch active before key on | Reset side switch |
| 11 | 38 | Incorrect start Attachment switch active before key on | Reset attachment switch |
| 12 | 39 | Incorrect start Tilt switch active before key on | Reset tilt switch |
| 13 | 40 | Lift analog value out of range | Lift analog fault or need to be calibrated |
| 14 | 43 | Steer analog value out of range | Steer analog fault or need to be calibrated |
| 15 | 44 | Traction controller speed protection | Vehicle speed is too high alarm ” |
| 16 | 45 | Traction controller encoder fault | 1、 Traction controller encoder fault 2、Traction motor speed sensor connection wire is open |
| 17 | 81 | Traction controller temperature is low | Traction controller temperature is low alarm |
| 18 | 82 | Traction controller temperature is high | Traction controller temperature is high alarm |
| 19 | 83 | Traction controller temperature sensor fault | Traction controller temperature sensor fault |
| 20 | 84 | Traction motor temperature is low | 1、 Traction motor temperature is low 2、 Traction motor temperature sensor is fault |
| 21 | 85 | Traction motor temperature is high | 1、 Traction motor temperature is high 2、 Traction motor temperature sensor is fault |
| 22 | 86 | Traction motor tenperature sensor fault | 1、 Traction motor temperature sensor is fault 2、Traction motor temperature sensor connection wire is open |
| 23 | 87 | Traction motor encoder fault | 1、 Traction motor encoder fault 2、 Traction motor speed sensor connection wire is open |
| 24 | 88 | DC bus voltage of traction controller is high | 1、 DC bus voltage high 2、 The ramp is too steep |
| 25 | 89 | DC bus voltage of traction controller is low | Need to charge or check power wiring |
| 26 | 90 | The default value of the traction controller is updated | Reset key |
| 27 | 91 | Traction drive limit | Battery low vehicle speed limit |
| 28 | 97 | Open drain of traction output open or short | Check the wire of open drain of traction output open or short |
| 29 | 98 | Traction controller over current or short | Check power wiring |
| 30 | 101 | Traction controller short | 1、 Check power wiring 2、 Controller enable before contactor pull |
| 31 | 102 | Traction controller temperature is high cut back | Traction controller temperature is high need cool |
| 32 | 103 | Traction motor temperature is high cut back | 1、 Traction motor temperature is high need cool 2、 Traction motor temperature sensor fault |
| 33 | 104 | Traction controller over current | 1、 Vehicle overload or Mechanical clamping 2、Traction motor speed sensor fault |
| 34 | 105 | Traction controller precharge failed | Replace the pre charge resistance |
| 35 | 110 | DC bus voltage of traction controller is low cut back | Battery need charge |
| 36 | 111 | DC bus voltage of traction controller is high cut back | DC bus voltage of traction controller is high cut back |
| 37 | 112 | DC bus voltage of traction controller is high cut back(Hardware monitoring) | DC bus voltage of traction controller is high cut back(Hardware monitoring) |
| 38 | 114 | Internal power supply error | Traction motor temperature sensor or speed sensor connection wire is open |
| 39 | 121 | Pump controller temperature is low | Pump controller temperature is low alarm |
| 40 | 122 | Pump controller temperature is high | Pump controller temperature is high |
| 41 | 123 | Pump controller temperature sensor fault | Pump controller temperature sensor fault |
| 42 | 124 | Pump motor temperature is low | 1、 Pump motor temperature is low 2、 Pump motor temperature sensor fault |
| 43 | 125 | Pump motor temperature is high | 1、 Pump motor temperature is high 2、Pump motor temperature sensor fault |
| 44 | 126 | Pump motor temperature sensor fault | 1、 Pump motor temperature sensor fault 2、Pump motor temperature sensor connection wire is open |
| 45 | 127 | Pump controller encoder fault | 1、Pump motor speed sensor fault 2、Pump motor speed sensor connection wire is open |
| 46 | 128 | DC bus voltage of pump controller is high | DC bus voltage of pump controller is high |
| 47 | 129 | DC bus voltage of pump controller is low | Check power wiring |
| 48 | 130 | The default value of the pump controller is updated | Reset key |
| 49 | 132 | Pump drive limit | Battery voltage low need charge |
| 50 | 137 | Open drain of pump output open or short | Check the wire of open drain of pump output open or short |
| 51 | 138 | Pump controller over current or short | Check power wiring |
| 52 | 141 | Pump controller short |  |
| 53 | 142 | Pump controller temperature is high cut back |  |
| 54 | 143 | Pump motor temperature is high cut back | Pump motor temperature is high alarm |
| 55 | 144 | Pump controller current calibration error | Reset key |
| 56 | 145 | Pump controller precharge failed | Replace the pre charge resistance |
| 57 | 150 | DC bus voltage of pump controller is low cut back | DC bus voltage of pump controller is low cut back |
| 58 | 151 | DC bus voltage of pump controller is high cut back | DC bus voltage of pump controller is high cut back |
| 59 | 152 | DC bus voltage of pump controller is high cut back(Hardware monitoring) | DC bus voltage of pump controller is high cut back(Hardware monitoring) |
| 60 | 153 | Pump controller CPU fault | Reset key |
| 61 | 154 | Pump controller speed control fault | Pump controller speed control fault |
| 62 | 157 | BMS over temperature protection | BMS over temperature protection |
| 63 | 158 | BMS single body over discharge | BMS single body over discharge need charge |
| 64 | 159 | BMS over voltage protection | BMS over voltage protection |
| 65 | 163 | BMS over current | BMS over current |
| 66 | 164 | Charge protection | Charge protection |
| 67 | 156 | Temperature protection | Temperature protection |
| 68 | 155 | BMS CAN bus off | BMS CAN bus off |
| 69 | 165 | Seat switch off after a period of time, the direction of the request to reset | Reset direction switch |
| 70 | 168 | BMS indicates Limit Current alarm | BMS indicates Limit Current alarm |
| 71 | 169 | BMS indicates cutoff Current alarm | BMS indicates cutoff Current alarm |
| 72 | 170 | BMS indicates brake Current alarm | BMS indicates brake Current alarm |
| 73 | 171 | BMS CAN Error | BMS CAN Error |
| 74 | 13 | HPG CONTROLLER EEPROM KO | Reset key |
| 75 | 30 | HPG CONTROLLER BATTERY VOLTAGE LOW | HPG CONTROLLER BATTERY VOLTAGE LOW NEED CHARGE |
| 76 | 33 | DC MOTOR VOLTAGE HIGH | RESET KEY |
| 77 | 49 | DC MOTOR OPERATING CURRENT IS ZERO | HPG CONRTOLLER SENSOR FAULT |
| 78 | 53 | HPG CONRTOLLER OVER CURRENT | HPG CONRTOLLER OVER CURRENT |
| 79 | 62 | HPG CONTROLLER TEMPERATURE HIGH | HPG CONTROLLER TEMPERATURE HIGH NEED COOL |
| 80 | 66 | HPG CONTROLLER BATTERY LOW | HPG CONTROLLER BATTERY LOW NEED CHARGE |
| 81 | 74 | HPG CONTROLLER DRIVER SHORTED | HPG CONTROLLER DRIVER SHORTED |
| 82 | 76 | HPG CONTROLLER COIL SHORTED | HPG CONTROLLER COIL SHORTED |
| 83 | 78 | HPG CONTROLLER VACC NOT OK | HPG CONTROLLER VACC NOT OK |
| 84 | 79 | HPG CONTROLLER INCORRECT START | HPG CONTROLLER INCORRECT START |
| 85 | 241 | HPG CONTROLLER CAN BUS KO | CHECK CAN WIRE OPEN AND CAN SPEED RATE |
| 86 | 242 | HPG CONTROLLER BATTERY OVER VOLTAGE | HPG CONTROLLER BATTERY OVER VOLTAGE |
| 87 | 243 | KEYOFF SHORTED | Key switch adhesion (HPG DC pump control fault) |
| 88 | 244 | HPG CONTROLLER WATCHDOG ERROR | HPG CONTROLLER WATCHDOG ERROR |
| 89 | 246 | HPG CONTROLLER WAITING FOR MAIN CONTACTOR | TURN OFF THE PUMP CONCTACTOR PARAMETER |
| 90 | 161 | DISPLAY CAN FAULT | CHECK DISPLAY AND CONTROLLER CAN CONNECTION |

# Chapter five Truck’s regular check and maintenance

Conduct a comprehensive pre-inspection of forklift trucks and forklifts to avoid failure and fail to produce the life it deserves. Maintenance program is based on the number of hours listed in forklift work 8 hours a day, working 200 hours a month the case may be, in order to maintain safe operation and maintenance procedures should be maintained on the forklift.

Routine maintenance and repair work carried out by the truck drivers, and other inspection and maintenance by professional maintenance personnel.

## Ⅰ.The check before operation

For safe operation and to make sure the truck in good condition, a comprehensive inspection of truck should be conduct before operation, which is a statutory duty. If find problems you should contact our sales department.

·A small mistake will cause a major accident, do not operate or move the forklift truck before the completion of repair work and inspections.

·The forklift should be checked on the platform.

·When checking on electrical system of the truck, the key switch should be switched off and the battery plug should be unplug before the test.

·Replacement of inappropriate handling of waste oil down (into the water pipe under the soil, burning, etc.) will pollute the water, soil, atmosphere, etc., which is prohibited by law.

### 1. Checking point and checking content

|  | No. | Checking points | Checking contents |
| --- | --- | --- | --- |
| Brake system | 1 | Brake pedal | Foot brake pedal travel and braking force |
|  | 2 | Brake oil | Quantity and cleanliness |
|  | 3 | Parking brake | Parking brake handle travel and the size of operation force |
| Steering system | 4 | Steering wheel control | Elastic, rotation and movement before and after |
|  | 5 | Hydraulic steering operation | Operation of all components |
| Hydraulic system and the frame | 6 | Function | Function, it has cracks, lubrication condition |
|  | 7 | Pipe | Whether the pipe is leakage |
|  | 8 | Hydraulic fuel | The appropriate fuel |
|  | 9 | Lifting chain | Left and right should be consistent with two chain tightness |
| Tyre | 10 | Tyre | Pressure size, whether abnormal breakage. |
|  | 11 | Wheel nut | Tighten firmly |
| Battery | 12 | Charging | Determine the battery capacity display status, the proportion of the plug should be firmly connected. |
| Lights, horn and switch | 13 | Headlights, taillights, reversing lights, horn turn signals, and emer- gency power off switch | To see if the light off, listening to speakers if sound, emergency power off switch is abnormal. |
| Detection and display | 14 | Function | When connected to key switch should display "test state normal" |
| Others | 15 | Owerhead guard, load backrest | Bolts, nuts are tightened |
|  | 16 | Nameplate and marks | Integrity |
|  | 16 | Other parts | Normal or not |

### 2. Checking procedure

(1) Check the brake pedal

Check brake condition and to ensure a fully depresses the brake pedal when the plane from the floor counting down the brake pedal travel should be more than 50mm, no-load forklift truck braking distance about 2.5m.

(2) Check the brake oil

·Open the lid and check the brake oil and other conditions.

(3) Check parking brake handle

- Push forward parking brake handle and observe following status.

- If there is proper pull jurney

- Brake force value

- Damaged parts or not

- Handle operating force value is suitable to operator or not

- Operator may adjust by the screw installed on the top of handle.

(4) Check the steering wheel rotation case

The steering wheel clockwise and counterclockwise rotating gently, check whether there is rebound phenomenon, a suitable spring trip to 50-100mm. Steering wheel before and after the trips

of about 7 °, if the above situation, turn the steering wheel shall be normal.

(5) Check the function of steering system

The steering wheel clockwise and counterclockwise rotation, check the power steering work.

(6) Check hydraulic system and frame function

Check the upgrade and after dumping the normal operation is smooth

(7) Check pipeline

Check lift cylinder, tilt cylinder, and all pipeline whether oil leak.

(8) Check the hydraulic oil

Land the fork to the ground, check oil level gauge hydraulic oily bits, when the oil level in the H to the L range, the volume of hydraulic point oil suitable range.

| model | H | L |
| --- | --- | --- |
| FE4P25-35Q | 28L | 32L |

(9) Check the lifting chain

Bring fork to the ground 200-300mm high, to ensure the tightness around the same chain. Check finger stick is in the middle, if different tightness can be adjusted through the chain joints.

·After adjustment, should be double nuts tighten.

(10) Check tires (pneumatic tires)

Unplug the nozzle cap, measuring tire pressure with a tire air pressure. After check air pressure, nozzle mouth should ensure that gas will not leak before installed the cap.

·Forklift tire pressure is higher than the car’s; it should not exceed the prescribed pressure value.

|  | model | tyre pressure |
| --- | --- | --- |
| front tyre | 28×9-15-14PR | 970 bar |
|  | 7.00-12-12PR | 860 bar |
|  | 7.00-12-16PR | 1000 bar |
| rear tyre | 6.00-10-10PR | 790 bar |
|  | 6.00-9-10PR | 860 bar |
|  | 6.00-9-12PR | 1030 bar |

Check tyre（solid tyre）

Check if there is dilapidation or leakage on tyre and its sides,and if there is deformation or damage in wheel rib and locking collar

(11) Check wheel nut

·Wheel nut loosening is very dangerous, if loose, the wheels may fall off, resulting in vehicle flip. Check the availability of loose wheel nut, it is very dangerous even one of them is loose, so be screwed to the provisions of pre-torque value.

Wheel nut tightening torque

Front wheel： 28X9-15-14PR     280-320N.m

7.00-12-12/16PR   280-320N.m

Rear wheel：  6.50-10-10PR     130-150N.m

6.00-9-10/12PR    130-150N.m

(12) Check charge condition

Measuring the proportion of battery, when converted to 30 ℃, the battery proportion from 1.275 to 1.285, indicating the battery is fully charged, and check whether the terminal block is loose, and whether the cable is damage.

(13) Check headlights, turn signals and horn

Check whether the normal bright lights, speakers is normal (when pressing the horn button, horn ring)

Check whether the emergency stop is normal.

| L | left steering light is bright |
| --- | --- |
| N | neutral |
| R | right steering light is bright |

(14) Check instrument panel features

Normally, after a few seconds turn the key switch, the dashboard will be the following graph shows

In addition to checking lights and operating conditions, the key switch must be turned off and disconnect the battery plug before check the electrical system.

## Ⅱ.Check after operation

After the completion of the work remove the dirt on forklift and check the forklift according to the follow items：

(1) Check all the parts if there is damage or leakage.

(2) If there is deformation, distortion, damage or breakage?

(3) Add lubricating grease according to the situation.

(4) Let fork upgrade to the max hight for several times after work. (When the daily work is not up to the fork with the arrival of the maximum height of the situation, it would allow oil flow through the tanks of the entire journey, to prevent rust.)

(5) Replace the faulty component which caused malfunction during work.

· A small mistake will cause a major accident. Do not operate or move the forklift truck before completion of repair work and inspections.

## Ⅲ.Truck cleaning

·Stop the truck at the specified location.

·Pull the parking brake handle.

·Press the emergency stop switch.

·Turn off the key switch and remove the key.

·Disconnect the battery plug.

### 1. Truck surface cleaning .

·Do not use flammable liquid to clean trucks, take safety measures to prevent short circuit.

·Use water and soluble detergent to clean the truck.

·Clean the oil filler and periphery of grease tap carefully.

If regular cleaning truck, please lubricate timely.

### 2. Chains cleaning

·Do not use chemical detergent, acids or other corrosive liquid to clean the chain.

·Place a tank in the bottom of the frame.

·Use gasoline or other petrochemical derivatives to clean the chain.

·Do not add any additive when use the steam nozzle cleaning.

·Dry immediately after cleaning of the chain pin and the water stain on chain surface.

### 3. Electric system cleaning

·Do not use water to clean the pump control and a variety of connectors, so as not to cause damage to electrical systems.

Use non-metallic brush or low-power hair dryer, according to the manufacturer instructions to clean the electrical system; do not move the protective cover.

### 4. After cleaning

·Thoroughly dry water stains on the truck (use compressed air as a example).

·Start the forklift according to the procedures.

·If moisture penetration into the motor, you must first remove the moisture, to prevent short circuits

 Moisture will reduce brake performance, brake truck briefly to drying the brake.

## Ⅳ.Regular maintenance

·Thoroughly dry water stains on the truck (use compressed air as a example).

·Start the forklift according to the procedures.

·If moisture penetration into the motor, you must first remove the moisture, to prevent short circuits

 Moisture will reduce brake performance, brake truck briefly to drying the brake.

### 1. Regular maintenance schedule

√—Check , calibration, adjustment  ×—Change

(1) Battery

| Maintena- nce item | Maintenance item | Tools | Every- day (8h) | Every week (50h) | Every month (200h) | Three months (600h) | Six months (1200h) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Battery | Electrolyte levels | Eye survey |  | √ | √ | √ | √ |
|  | Electrolyte specific gravity | Gravi- meter |  | √ | √ | √ | √ |
|  | Quantity of electricity |  | √ | √ | √ | √ | √ |
|  | Terminals are loose |  | √ | √ | √ | √ | √ |
|  | The cable is loose |  | √ | √ | √ | √ | √ |
|  | Surface cleaness of the battery |  | √ | √ | √ | √ | √ |
|  | Battery surface has placed Tools |  | √ | √ | √ | √ | √ |
|  | Ventilation cover is tightened, vent is unimpeded |  |  | √ | √ | √ | √ |
|  | Away from the fireworks |  | √ | √ | √ | √ | √ |

（2）Controller

| Maintena- nce item | Maintenance item | Tools | Every- day (8h) | Every week (50h) | Every month (200h) | Three months (600h) | Six months (1200h) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Controller | Check the wear condition of contactors |  |  |  |  | √ | √ |
|  | Check if contactor mechanical movement is good |  |  |  |  | √ | √ |
|  | Check micro switch operation of the pedal is normal |  |  |  |  | √ | √ |
|  | Check if the motor, battery and power unit is a good connection |  |  |  |  | √ | √ |
|  | Check if the malfunction analysis system is normal |  |  |  |  |  | At the begin- ning of 2 years |

（3）Motor

| Maintena- nce item | Maintenance item | Tools | Every- day (8h) | Every week (50h) | Every month (200h) | Three months (600h) | Six months (1200h) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Motor | Remove the eyewinker from the motor shell |  |  |  | √ | √ | √ |
|  | Clean or change bearing |  |  |  |  |  | √ |
|  | IfCarbon brushes, commutator is worn, the spring force is normal |  |  |  | √ | √ | √ |
|  | If Wiring is correct, reliable |  |  |  | √ | √ | √ |
|  | Clearing brush and commutator surface for the film end on toner |  |  |  |  | √ | √ |

（4）Transmission system

| Maintena- nce item | Maintenance item | Tools | Everyday (8h) | Every week (50h) | Every month (200h) | Three months (600h) | Six months (1200h) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Gearbox and Wheel Reducer | Noises |  | √ | √ | √ | √ | √ |
|  | Check leakage |  | √ | √ | √ | √ | √ |
|  | Change oil |  |  |  |  |  | × |
|  | Check the working condition of brake |  | √ | √ | √ | √ | √ |
|  | Check the moving of qear wheel |  |  |  |  | √ | √ |
|  | Check the junction with the frame bolts loose situation |  |  |  | √ | √ | √ |
|  | Check wheel bolt tightening torque | Torque wrench | √ | √ | √ | √ | √ |

（5）Wheel(forward, backward wheel)

| Maintena- nce item | Maintenance item | Tools | Every- day (8h) | Every week (50h) | Every month (200h) | Three months (600h) | Six months (1200h) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Tyre | Wear, cracks or damage |  | √ | √ | √ | √ | √ |
|  | If there is nails,stone or other foregn items on tire matter |  |  |  | √ | √ | √ |
|  | Wheel damage |  | √ | √ | √ | √ | √ |

（6）Steering system

| Maintena- nce item | Maintenance item | Tools | Every- day (8h) | Every week (50h) | Every month (200h) | Three months (600h) | Six months (1200h) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Steering wheel | Check clearance |  | √ | √ | √ | √ | √ |
|  | Check axis loose |  | √ | √ | √ | √ | √ |
|  | Check radial losse |  | √ | √ | √ | √ | √ |
|  | Check operation condition |  | √ | √ | √ | √ | √ |
| Steering gear and valve block | Check if mounting bolts are loose |  |  |  | √ | √ | √ |
|  | Check valve block interface with steering leak case |  | √ | √ | √ | √ | √ |
|  | Check seal of connectors |  | √ | √ | √ | √ | √ |
| Rear-axle | Check whether the rear axle mounting bolts loose |  |  |  | √ | √ | √ |
|  | Check if there is bending, deformation, cracks or damage |  |  |  | √ | √ | √ |
|  | Check or replace the lubrication of bridge bearing. |  |  |  |  | √ | √ |
|  | Check or replace lubrication of bridge bearing |  |  |  |  | √ | √ |
|  | Check steering cylinder operating conditions |  | √ | √ | √ | √ | √ |
|  | Check whether steering cylinder is leaking |  | √ | √ | √ | √ | √ |
|  | Check rack and pinion gear case |  |  |  |  | √ | √ |
|  | wiring and working condition of sensor |  |  |  |  | √ | √ |

（7）Brake system

| Mainten- ance item | Maintenance item | Tools | Every- day (8h) | Every week (50h) | Every month (200h) | Three months (600h) | Six months (1200h) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Brake pedal | Empty run | Gradu- ated scale | √ | √ | √ | √ | √ |
|  | Pedal travel |  | √ | √ | √ | √ | √ |
|  | Operation condition |  | √ | √ | √ | √ | √ |
|  | Whether there is air in the brake pipe |  | √ | √ | √ | √ | √ |
| Stop, brake and control | Whether the brake is safe and has enough travel |  | √ | √ | √ | √ | √ |
|  | Operation condition |  | √ | √ | √ | √ | √ |
| Pole and cable | Operating performance |  |  |  | √ | √ | √ |
|  | Whether the connection is lossen |  |  |  | √ | √ | √ |
|  | Wear of reduction gearbox connectors |  |  |  |  | √ | √ |
| pipe | Damage, leakage, rupture |  |  |  | √ | √ | √ |
|  | Loose situation of connection and clamping parts |  |  |  | √ | √ | √ |
| Brake pump | Leakage situation |  | √ | √ | √ | √ | √ |
|  | Check oil level, oil changing. |  | √ | √ | √ |  | × |
|  | Pump situation |  |  |  |  | √ | √ |
|  | Pump leakage, damage |  |  |  |  | √ | √ |
|  | Pump piston cups, one-way valve wear damage, replace |  |  |  |  |  | × |

（8）Hydraulic system

| Maintena- nce item | Maintenance item | Tools | Every- day (8h) | Every week (50h) | Every month (200h) | Three months (600h) | Six months (1200h) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Hydraulic oil tank | Check the oil, oil change |  | √ | √ | √ | √ | × |
|  | Suction filter cleaning |  |  |  |  |  | √ |
|  | Exclude eyewinker |  |  |  |  |  | √ |
| Control lever | Whether the connection is lossen |  | √ | √ | √ | √ | √ |
|  | Operation condition |  | √ | √ | √ | √ | √ |
| Multitandem valve | Leakage |  | √ | √ | √ | √ | √ |
|  | Safety valve and self-locking tilt valve operation condition |  |  |  | √ | √ | √ |
|  | Measuring the pressure of the safety valve | Oil gauge |  |  |  |  | √ |
| Pipeline joint | Leakage, loosening, fracture, deformation, damage |  |  |  | √ | √ | √ |
|  | Change the tube |  |  |  |  |  | × 1～2years |
| Hydraulic pump | Hydraulic pump is leaking or there is noise |  | √ | √ | √ | √ | √ |
|  | Hydraulic pump gear wear |  |  |  | √ | √ | √ |

（9）Lifting system

| Maintena- nce item | Maintenance item | Tools | Every-day (8h) | Every week (50h) | Every month (200h) | Three months (600h) | Six months (1200h) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Chain and chain wheel | Check the chain tension state, whether deformation, corrosion damage |  | √ | √ | √ | √ | √ |
|  | Fuel chain |  |  |  | √ | √ | √ |
|  | Rivet pin and loose conditions |  |  |  | √ | √ | √ |
|  | Chain wheel deformation, damage |  |  |  | √ | √ | √ |
|  | If Bearings of chain wheel loosen |  |  |  | √ | √ | √ |
| Attachment | Check whether in normal state |  |  |  | √ | √ | √ |
| Lifting and tilt cylinder | Whether Piston rod, piston rod thread and the connection is loose, deformation, damage |  | √ | √ | √ | √ | √ |
|  | Operating conditions |  | √ | √ | √ | √ | √ |
|  | Leakage |  | √ | √ | √ | √ | √ |
|  | abrading and damaging status of pin and oil cylinder |  |  |  | √ | √ | √ |
| Fork | Damage,deformation,wear of fork |  |  |  | √ | √ | √ |
|  | Damage,deformation,wear of allocation pin |  |  |  |  | √ | √ |
|  | cracking and abrading status in hooker welding of fork root |  |  |  | √ | √ | √ |
| Mast fork frame | welding between inner mast,outer mast and beam is cracking or damaged or not |  |  |  | √ | √ | √ |
|  | Tilt cylinder bracket and the door frame weld whether cracking, damage |  |  |  | √ | √ | √ |
|  | Inner frame, outer frame weld whether cracking, damage |  |  |  | √ | √ | √ |
|  | Fork frame weld whether cracking, damage |  |  |  | √ | √ | √ |
|  | wheel loosen |  |  |  | √ | √ | √ |
|  | Mast bearing wear, damage |  |  |  |  |  | √ |
|  | Mast bearing cap bolts whether loose |  |  |  | √ |  | √ |
|  | Whether Lift cylinder rod bolt head, bending plate bolts loose |  |  |  | √ |  | √ |
|  | cracking,damaging status of welding of roller and roller shaft |  |  |  | √ | √ | √ |

（10）Else

| Maintena- nce item | Maintenance item | Tools | Every- day (8h) | Every week (50h) | Every month (200h) | Three months (600h) | Six months (1200h) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Overhead guard and load backrest | Installation is firmly | Measur-ing hammer | √ | √ | √ | √ | √ |
|  | Check the deformation, cracking, damage |  | √ | √ | √ | √ | √ |
| Indicator light for steering | Work and installations |  | √ | √ | √ | √ | √ |
| Horn | Work and installations |  | √ | √ | √ | √ | √ |
| Lamps and bulbs | Work and installations |  | √ | √ | √ | √ | √ |
| Reversing Buzzer | Work and installations |  | √ | √ | √ | √ | √ |
| Instrument | Working condition |  | √ | √ | √ | √ | √ |
| Wire | Harness injury, loosening |  |  | √ | √ | √ | √ |
|  | Electrical connection loose |  |  |  | √ | √ | √ |

### 2. Regular replacement of key safety parts

Periodic replacement of critical safety components.

When some parts difficult to find through regular maintenance of injury or damage, in order to further improve security, the user should replace the parts given in the following table for regular.

If the parts appeared abnormal before the time comes to replace, it should be replaced immediately.

| Name of critical safety components | Useful life |
| --- | --- |
| Brake tube or hard pipe | l～2 |
| Hydraulic hose for lifting system | l～2 |
| Lifting chain | 2～4 |
| High pressure hose/tube for hydraulic system | 2 |
| Oil cup of brake fluid | 2～4 |
| Cylinder cover and dust cover of brake pump | 1 |
| Internal hydraulic system seals, rubber parts | 2 |

## Ⅴ.Area lubricated and lubricant recommended

### 1. Area lubricated

○：Change                       FO： Hydraulic oil

◎：reinforce                     GO： Gear oil

□：Check and adjust	     CG： Grease

BO： Brake fluid	         W： Distilled water

### 2. Lubricant recommended

| Name | Trademark | Capability(L) | Remark |
| --- | --- | --- | --- |
| Hydraulic oil | L-HM32 | Max30 | ≥-5℃ |
|  | L-HV32 |  | ≥-20℃ |
| Gear oil | 85W/90GL-5 | 4.5 | -15℃ ~ +49℃ |
|  | 80W/90GL-5 |  | -25℃ ~ +49℃ |
| Brake fluid | Caltex DOT3 | 0.2 |  |
| Industrial Vaseline | 2# |  | Battery electrode column |
| Grease | 3# Lithium Grease |  |  |

### 3. Hydraulic Schematic Diagram

| 1、Hydraulic oil tank | 2、Oil absorption filter | 3、Pump motor |
| --- | --- | --- |
| 4、Gear pump | 5、Steering device | 6、Multiple directional control valve |
| 7、Steering cylinder | 8、Governor valve | 9、Shut-off valve |
| 10、Lifting cylinder | 11、Tilt cylinder |  |

### 4. labeling

Signs sticked on vehicle are to illustrate using method and attention matters of vehicle,which not only takes consideration of you but also of the vehicle.stick the signs plate on again if they fall off.

| 1、nameplate | 2、load curve | 3、Use the information | 4、 lubrication chart |
| --- | --- | --- | --- |
| 5、warning sign | 6、Read the tip | 7、Lifting point | 8、vehicle lifting |
| 9、Tire pressure | 10、No lifting point | 11、Company logo | 12、Model identification |
| 13、Charging logo | 14、Squeeze the hand signs | 15、Seat belts | 16、Prohibited to climb |
| 17、warning sign | 18、Lifting point |  |  |

# Chapter six Truck’s Lithium battery use and safety

### 1. Safety operation procedures

Safety precautions for lithium batteries

△  Lithium batteries should be kept far away from the dangerous chemicals, fire, dust and other extreme environments.

△ Incorrect use may lead to external short circuit, overcharge, the temperature is too high, causing the battery to smoke, if this happens please promptly cut off the power, unplug the power plug, use fire extinguisher to keep safe.

△ The incorrect use may cause the battery internal expansion, will lead to serious rupture, should immediately stop using it if it is detected, turn off the vehicle power, unplug the power plug, and contact our customer service immediately.

△ Do not disassemble, extrusion, puncture, keep in high temperature environment, or baking battery, avoid high-frequency vibration, external shocks, crashes for the battery.

△ Do not short connect, avoid any metal or other conductive objects touch the positive and negative poles of the battery expect the pressing bolt or conductive tape of the battery.

△ It is prohibited to expose the battery in the environment with temperature at 55℃ or above for long time, no heating or put the battery into a fire.

△ It is strictly prohibited to use the charger without proper charging protection device (Lithium battery protection circuit board, battery management system etc.) or use the battery charging equipment which is not approved by the Lithium manufacturer (charger, DC power supply lamp)

△ It is prohibited to disassemble the battery by technicians not authorized by the manufacturer.

△ The battery is prohibited to be put in the water.

△ Children or any other people who lack of lithium battery safety knowledge are forbidden to use the product.

△ It is prohibited to connect the battery with other batteries or similar type of batteries in series or in parallel.

△ It is prohibited to connect the battery sets with battery protection circuit board or battery management system in series or in parallel.

#### Warning

#### Battery storage for a long time (storage time for more than 6 months or more), need to cut off the power of the lithium battery completely, it is recommended not to store the battery less than 60% of the capacity, storage environment humidity is not higher than 95%RH.

#### Within a specified period of time, charge and discharge the battery according to the requirements of storage.

| Storage environmental temperature | storage environmental relative humidity, | storage time |
| --- | --- | --- |
| -10～0℃ | 5%～95% | ≤6 months 60%SOC |
| 0～40℃ | 5%～95% | ≤6 months 60%SOC |
| 40～45℃ | 5%～95% | ≤2 months 60%SOC |

### 2. Introduction and application requirements of lithium batteries

2.1 Product Brief Introduction

Lithium phosphate lithium ion battery has good safety, small resistance, volume and quality characteristics of high specific energy, long cycle life, suitable for application s for all kinds of electric forklifts, electric buses, electric motor car, it has been widely used and get the praise of our customers.

Lithium phosphate Lithium ion battery is a lithium ion battery using lithium phosphate as cathode materials, the main application direction is for the power battery, has the characteristics of small volume, light weight, long cycle life, high safety, pollution-free, lithium phosphate The size and space of the lithium ion battery compare to lead-acid battery with same capacity is about 2/3 of the lead-acid battery, and weighs only 1/3 of . The cycle life of ordinary lead-acid battery in about 1000 times, the highest of 1200 times, a forklift for lithium ion battery cycle life can be up to 4000 times, so the performance/price ratio in the same conditions of use of lithium phosphate lithium ion battery is much higher than the lead-acid battery

Lithium phosphate lithium ion battery are subjected to rigorous testing, capacity, storage capacity, high discharge, low discharge, discharge rate and other performance indicators exceeded the national standard, puncture, extrusion, vibration, short circuit, overcharge, over discharge and other safety performance indicators fully meet the national standard, no risk of fire and explosion.

Lithium phosphate lithium-ion batteries do not contain any heavy metals and rare metals, there is no hazardous material to any human and environmental is used for re-manufacture and use of the battery, it is the world's most environmentally friendly battery.

Warning： Please use the package in strict accordance with the package instructions, otherwise it may not be included in the warranty:

- Please do not operate electric vehicles equipped with lithium batteries at temperatures above 55 ℃ or below -20 ℃

- Please charge immediately after the use of the vehicle in environment with temperature lower than 0℃

- Please do not flush the battery box directly to prevent the water entering from the battery box.

- If you are not professionals, please do not touch, move, disassemble batteries and corresponding high-voltage cables, or other components with high voltage warning signs

Attention：

- In order to achieve better use effect and prolong the battery life, contact the manufacturer every year and check the battery performance and balance charging by the manufacturer and technician

- If a vehicle is hit strongly during transit, stop the vehicle in the safe area and check whether the vehicle battery pack area is damaged

- When a vehicle or battery pack catch on fire, left the vehicle to a safe distance quickly, use dry powder fire extinguisher to stop the fire, use water to extinguish or incorrect fire extinguishers may cause electric shock, according to the characteristics of the battery, the battery capacity within warranty period should reduce from 0% to 25%.

  - Working temperature of lithium battery

- Charging temperature range: 0~40℃, charge the battery in low temperature environment below 0℃ with high rate will cause damage to the battery. Please charge immediately after the use of the vehicle in environment with temperature lower than 0℃

- Discharging temperature range: -20 to 50 ℃, the discharge capacity in low temperature (-20 to 0 ℃) is lower than the normal temperature. The battery can be used at 40~50 ℃ ambient temperature, but if the battery temperature is too high, especially the battery in the long time high temperature environment, will accelerate the battery internal material aging, shorten the battery life, it is not recommended to use long at this temperature.

- Environmental temperature over the above range of charge and discharge temperature, will have a negative impact on the performance of batteries or damage, may shorten the service life of the battery, please avoid.

According to the chemical properties of lithium ion batteries, in normal use, the internal energy of chemical reactions between normal and chemical, but under certain conditions, such as the overcharge, over discharge and overcurrent will lead to abnormal chemical reactions occurring inside the battery, it will seriously affect the performance of the battery and service life, and may produce large amounts of gas, so that the internal pressure of the battery increases rapidly after the resulting cell bulging failure, therefore all lithium-ion batteries need a protection circuit for effective monitoring of the charge and discharge state of battery, and in some conditions to turn off the charge and discharge circuit to prevent damage to the battery.

Protection circuit usually includes overcharge protection, over discharge protection, over-current protection, temperature protection, short-circuit protection, insulation protection, etc., so as to effectively protect the normal use of batteries.

  - Working principle of lithium ion battery:

Lithium iron phosphate battery: a lithium ion two cell using lithium iron phosphate as cathode material,

The chemical equation for charging and discharging is as follows:

During charging:

The external current flows from the negative to the positive electrode, causing the lithium ion in the positive electrode to Li+ out of the lithium iron phosphate lattice, passing through the diaphragm to the negative electrode, and embedded in the layered structure of the negative electrode of the carbon material.

During discharging:

The lithium ion Li+ in the negative electrode is removed from the carbon material layer and moves to the positive electrode through the diaphragm and is embedded in the lattice of the positive material, and accordingly, the current flows from the positive electrode to the negative electrode through an external load.

### 3. Charging operation instructions for lithium batteries

Caution: safety precautions before charging

Please choose to charge in a relatively safe environment (avoid liquid, fire, etc. extreme environment)

Please keep necessary fire extinguishing equipment (dry powder fire extinguisher) near the charger, emergency firefighting can be carried out in extreme cases

Please make sure there is no dust, water or other articles in the charging plug and charging socket before charging, if there is any,  please clean it  before charging, otherwise it will lead to the bad connection between the charging plug and charging socket, cause heat and even cause a fire.

Do not modify and disassemble the charging port and charging equipment, which may lead to charging failure and fire. According to the characteristics of the battery, the battery capacity within warranty period should reduce from 0% to 25%.

- Charging operation steps:

1) The forklift stops stable and turn off the key switch

The forklift is stationary and ensures that the key switch in the charging vehicle is in a turn-off position. Open charging door and protective cover.

2) Socket port check

Take off the charging gun from the charger, check the charging gun and the lithium battery charging socket on the vehicle, make sure there is no water or other articles in the port, and the metal terminal is not damaged or affected by rust or corrosion.

3）Instrument display in standby mode;

Power switch is on the rear side of the charger, turn on the power switch of the charging equipment, charging equipment is on with indicator lights, display shows  welcome screen as shown in the graph, charger will enter into the standby mode after self-checking, showing the battery voltage, current and charging power, due to charging gun is not connected to the truck at this time, so state of charging displays "Please connect the battery".

4）Complete the charging connection and the normal charging display

Remove the charging gun, insert the gun into the body end lithium battery charging socket, charger will complete the self-checking and communication with the lithium battery, when there is no fault for the whole system, the charger internal relay will work, charging indicator is on, and the instrument will display the charging voltage, charging time and charging current and fault information.

5）Charging end display and power off operation

When the lithium battery is full, the charger will automatically stop charging, at this time, the green light indicating the battery has full voltage and output meter on the output current is 0, then press the pause button, then unplug the charger gun (Note: the charging gun head is integrated with the lock button as shown in Figure (b) must be pressed to be normal plug operation), winding gun line, out back the charging gun

If the lithium battery is not fully charged, it is necessary to press the stop button. When the charging current is reduced to 0 (A), the charging gun head can be pulled out.

Cover the charging cover and the door of the forklift, turn off the charger power and end the charging.

Caution: to avoid serious personal injury, the following precautions should be taken when the forklift is charging!

- Do not touch the charging terminals or metal terminals in the charger head.

- When there is lightning, do not charge the vehicle or touch the vehicle. Lightning strikes may cause damage to the charging equipment and cause personal injury.

- After the end of charging, do not use wet hands or stand in the water to disconnect the charging device, because this may cause electric shock, causing personal injury.

- After the charging is finished, please turn off the forklift charging port protection cover, to avoid any objectives enter into charging plug or socket of the forklift, which will lead to charging port damage.

Note: in order to avoid damage to the charging equipment, please pay attention to the following matters

- Do not turn off the charging port door when the charging port is open;

- Do not pull or twist the charging cable;

- Please do not impact the charging equipment;

- Do not store or use charging equipment at temperatures above 55 ℃;

- It is prohibited to direct unplug the charging gun when there is still charging current, which may cause arcing phenomenon, causing the loss of property and personal injury;

- Do not put charging equipment near the heater or other heat sources.

### 4. Structure and main technical parameters of lithium battery

4.1 Structure of lithium battery

Introduction of name and function of main parts :

1. Debug1 RS485. Connect the serial port of the lithium battery BMS system and connect the handheld monitor or the PC por.

2. Alarm. Lithium battery fault alarm

3. Power LED. The lithium battery switch is closed when the light is on.

4. Communication port. Communication port for lithium battery and controller,

realizing communication connection between lithium battery and controller.

5. Debug1 CAN. Connect the serial port of the lithium battery BMS system and connect the handheld monitor or the PC por.

6. Power supply positive pole connecting end

7. Negative terminal of power supply

8. Fan. Air outlet

9. Fan. Air intake

10. Charging socket. When the lithium battery is charged, the cover is opened and the charging gun is inserted, and the charging of the lithium battery can be completed.

11. Power plugs. Battery connection plug for lithium battery and forklift.

4.2 Main technical parameters

| Forklift Model |  | FE4P25-28Q | FE4P30-35Q |
| --- | --- | --- | --- |
| Lithium battery Capacity | STD | Ah | 200 | 200 |
|  | OPT | Ah | 300 | 300 |
|  | OPT | Ah | 400 | 400 |
|  | OPT | Ah | 554 | 554 |
| Battery weight | Kg | 215-450 | 215-450 |
| Nominal voltage | V | 80 |
| Operating voltage range | V | 70-92 |
| Rated charging current | A | 65A/100A/150A/200A |
| Charging temperature | ℃ | 0～40 |
| Discharging temperature | ℃ | -20～55 |

Attachment: lithium battery system diagnosis code and processing method

| Battery System Failure Maintenance Table |
| --- |
| SN | Fault Type | Posible Cause | Detect Methord | Cause Comfirmed | RecoverySolution |
| 1 | Battery pack has no output after starting, switch indicator is not on | 1. The internal components of the system are damaged; 2. The system voltage is over discharge. | 1. measure the total positive and negative voltage with the pen to check whether the total voltage of the system is normal. | <36V, the DCDC converter can not work. |  |
|  |  |  | 2. Choose the multimeter to guide the gears and measure whether the panel communication wire harness S1_A and S1_B are normally connected. | Wire harness failure due to abnormal conduction at both ends of wire harness | Replace wire harness |
|  |  |  | 3. After measuring the normal connection of the voltage wiring harness, press the start switch to check whether the BMS is on. | After pressing the start switch, the BMS does not turn on the light, preliminary judgment of BMS faul | Replace BMS or DCDC |
| 2 | There is no power on the forklift after the battery pack starts, and the battery indicator light is on. | 1. Abnormal communication with forklift 2. Damage of internal components of the system | . check the alarm code on the forklift display screen to confirm the specific fault. 2,If it is confirmed as a CAN communication problem, disconnect the discharge connector and measure whether there is 120_resistance on the CAN ports. | 1. if the resistance iis Infinity , that the CAN communication cables are disconnected. First, comfrim the normal conduction of CANH and CAN between the discharge connector and the panel communication port. And then confirm the conduction between the panel and BMS. 2 the internal CAN chip of BMS may be damaged if there is resistance, but it is much larger than 120 | 1. Replacement of damaged wiring cables; 2. Replacement of damaged BMS |
|  |  |  | 1. Disconnect the discharge plug and start the battery pack separately to check whether the discharge plug has output | If there is an output, the internal circuit of the locomotive may be wrong, resulting in the failure of the battery pack to output. | Check forklift communications and power cables |
|  |  |  | 1. Remove the battery case cover and the eletrical case cover to check whether the fuse is normal | Fuse demaged | Before replacing the fuse, the short circuit between positive and negative discharges of locomotive and battery pack should be measured. If there is no short circuit, the fuse should be replaced. If there is, the short circuit fault should be dealt with first, and then the fuse should be replaced. |
| 3 | Battery pack can't be recharged. Battery pack indicator light is on | 1. Abnormal communication with forklift truck; 2. Damage of internal components of the system | 1. Measure whether the 12V, GND, CANH and CNAL wiring harnesses of charging sockets are conducting normally. | Abnormal conduction | Replace wire harness |
|  |  |  | 2. Connect the charger, check the fault code of the charger display screen, check whether the charging port terminal is loosened or not, and check whether there is 120_resistance at both ends of CAN communication. | No 120_resistance was measured and the CAN chip was damaged. | Replace BMS |
| 4 | Battery pack can not be charged, battery pack indicator is not on | 1. Charger without 12V auxiliary power supply output; 2. Damage of internal components of the system | 1. Disconnect the charger and battery pack, and measure whether there is 12V auxiliary power output after the charger is turned on separately. | NO 12V output | Replace or repair the charger |
|  |  |  | 2. Measure whether charging socket wiring harness 12V, GND wiring harness is normal | Abnormal wiring harness conduction | Replace wire harness |
|  |  |  | 3. Confirm that the output of 12V auxiliary power supply of charger is normal and the wiring harness of charging socket is normal. Keep charger on and connected with battery pack to check whether BMS is on. | Preliminary judgement of BMS fault | Replace BMS |
| 5 | Battery Pack Can't Shut Down | Damage of internal components of battery pack system | 1. The key switch of the car is short circuit; 2. The internal components of the battery pack system are damaged | The battery pack can switch the locomotive on and off normally, and the locomotive switch wiring harness is short-circuiting | Check forklift switch harness |
|  |  |  | 2. Disconnect the battery pack from the forklift truck and press the switch button on the battery pack. The battery pack can not shut down normally. After the battery box panel is removed, the wiring harness on the switch is disconnected, and the power can be shut down normally. | SWITCH demaged | Replace SWITCH |
|  |  |  | 3. The battery pack can not be shut down after disconnecting the connection between the battery pack and the forklift truck and the wiring harness on the switch. 。 | BMS fault | Replace BMS |

### 5 Transportation

- Handling and transportation should avoid severe vibration, greater external impact, no throwing, rolling, upside down, extrusion, and excessive stacking;

- Avoid getting caught in the rain during transit;

- During transit, make sure the battery is disconnected from the vehicle and charging equipment without any form of charging and discharging.

NOBLELIFT INTELLIGENT EQUIPMENT CO.,LTD.

Service hotline：4008-836115

Wechat：nuolijixie

Postcode：313100   Email address: info@noblelift.com

Website：www.noblelift.com

Version：Dec,2021

# Text boxes

Emergency switch

Rear view mirror

front big light

front light unit

cornering lamp

rear light unit

Put fatigue dress on before driving!

| 1 | Parking | 13 | Steering Angle |
| --- | --- | --- | --- |
| 2 | Seat | 14 | Display Menu |
| 3 | Brake Pedal | 15 | Display Menu |
| 4 | Lift lock | 16 | Display Menu |
| 5 | Fault alarm | 17 | Display Menu |
| 6 | Safety Belt | 18 | H Mode |
| 7 | Forward/Reverse | 19 | S Mode |
| 8 | Battery level | 20 | E Mode |
| 9 | Working Time | 21 | Tortoise Mode |
| 10 | Travel Speed | 22 | Cancel/- |
| 11 | Speed Mode | 23 | Enter/+ |
| 12 | Control Fault | 24 | Nothing |

| 1 | Tortoise speed | 13 | Battery level |
| --- | --- | --- | --- |
| 2 | Fault alarm | 14 | Travel Speed |
| 3 | Battery alarm | 15 | Steering Angle |
| 4 | Lift lock | 16 | Forward/Reverse |
| 5 | Seat | 17 | Speed Mode |
| 6 | Parking | 18 | Working Time |
| 7 | Cancel |  |  |
| 8 | Enter |  |  |
| 9 | Tortoise Mode |  |  |
| 10 | P Mode |  |  |
| 11 | E Mode |  |  |
| 12 | S Mode |  |  |

Brake pedal

Brake grease nipple cap

Brake grease nipple

Oil box

content gage

Lifting chain □◎CG

Steering system □◎CG

Brake cylinder◎ BO

Brake pedal □

Mast bearing support ◎CG

Tilt cylinder pin◎ CG

Direction pipe column◎ CG

Drive axle ◎□CG

Charging

Discharging